## Slide 1: Development of beam tracking detector using MicroChannel Plate(MCP)
2012. 12. 15
Chung-Ang Univ.
Il Maek Lee

## Slide 2
Outline.
Introduction
Research goal
Research contents and methods
Research schedule
Current progress
Summary

## Slide 3
Introduction
Case of In-Flight RI Beam with relatively large Beam emittance,
each heavy ion particle trajectory tracking is needed.
Install the detector at each point to obtain 2-dimensional information.
Contribution of the particle trajectory and the beam profile monitor using a 2-demension information.
detector 1
detector 2
Target
Z1
Z2
(X1, Y1)
(X2, Y2)
Target size

## Slide 4
MCP is made by thin tube that has diameter 10㎛ in circular shape.
Incident electrons generate secondary electrons by collision on the wall of channel. Secondary electrons collide again. Signal is amplified by this processes.
In general we obtain amplified signal with 103~105 times.
About MCP.
Introduction

## Slide 5
In general Electrons, ion, UV ray, X-ray, and γ-ray detection use MCP.
Used to connect the 1~3 MCP to obtain the desired gain.
MCP is small energy loss and no background because of thinner than the thickness of the PPAC. So suitable Low energy Heavy ion experiment.
About MCP.
Introduction

## Slide 6
Efficiency :
36Ar : 100 % @ < 5 kHz
11C : > 96 % @ 500kHz
18F : > 80 % @ 700kHz, > 55% @ 1MHz
Position resol : X - 1.2 ± 0.1 mm (FWHM) Y - 2.8 ± 0.1 mm (FWHM)
Time resol : 0.7 ~ 0.8 ns
Position resolution is bad because of reflector structure
Hayakawa Model
Introduction

## Slide 7
Expected beam conditions. a. Intensity > 106pps b. Purity ~ 100% c. E/A ≤ 18 MeV
MCP : Efficiency : 100% (E < 10MeV/u, Z/A < 0.6)
Position resol. : < 1mm (FWHM)
Time resol. : < 1 ns (FWHM)
Research goal

## Slide 8
Previous research
Simulation
Prototype manufacturing
Beam test using a radioactive source and the domestic and international facilities
Optimized design values obtain and apply
Design
Research contents and methods

## Slide 9
 | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May
Previous Research |  |  |  |  |  |  |  |  | 
Simulation |  |  |  |  |  |  |  |  | 
Prototype Manufacturing / Optimization |  |  |  |  |  |  |  |  | 
Design |  |  |  |  |  |  |  |  | 
Research schedule

## Slide 10
GANIL Model
Efficiency : near 100%
(E>50MeV/nucleon, Z>8)
Position resol : > 0.2mm
Time resol : 200~300ps
The best efficiency : 200~500eV
The best acceleration potential : 100~400V
Current progress

## Slide 11
GANIL Model
Current progress
Lorentz force
θ
O
ρ
r
Electron
One hole of the MCP
r-rcosθ
rsinθ

## Slide 12
GANIL Model
d : distance of foil~sensewire
B : intensity of b-field
Vacc : acceleration of equipotential
Current progress

## Slide 13
Improve position resolution using B-field
GANIL Model
E=4000V/m, without B-field
E=4000V/m, B=3.0mT
Beam monitoring area is smaller than MCP size because of oblique structure.
Current progress

## Slide 14
Design concept for Simulation
Electron
Beam
MCP
Sensewire matrix
Equipotential plates
Electromagnet
E-field
B-field
Current progress

## Slide 15
Design concept for Simulation
Current progress
n = 2
d = 0.025m >> 25mm
Vacc = 2000V
B = 0.003T >> 3mT

## Slide 16
Design E-field using FEMM
Current progress
wire diameter : 1um
wire spacing : 5mm

## Slide 17
Design E-field using FEMM
Current progress
V = -1900V~-100V

## Slide 18
Design E-field using FEMM
Current progress
|E| = 74500 V/m

## Slide 19
Design B-field using FEMM
Current progress
Copper 18 AWG
Coil : 500
Current : 0.5Amps
Center : 2.8mT~3.15mT
Side : 3.2mT~3.85mT

## Slide 20
Simulate using FEMM
Current progress

## Slide 21
Simulate using FEMM
Current progress

## Slide 22
Simulate using FEMM
Current progress
No wire
-2041V ~ -2036V
-2042V ~ -2008V
Wire
-2035V ~ -2025V
-2040V ~ -1850V

## Slide 23
Simulate using octaveFEMM
Current progress
y : -50
X range : -1 ~ 1
y : -50
X range : -0.5 ~ 1.5

## Slide 24
Limit of FEMM
Current progress
Problem solves magnetic or electrostatic.
Planar or axisymmetric.
limit of 2-dimension problem.
Lorentz force is 3-dimension problem.
Need to solve the electrostatic and magnetic at the same time and to support 3-dimension problem.

## Slide 25
Conclusions
Current progress
Acceleration potential is positive.
The results obtained use to design.
Add B-field in this concept design.
3-dimension simulate using MAFIA
EM-field simulation.

## Slide 26
Summary
Case of In-Flight RI Beam each heavy ion particle trajectory tracking is needed.
MCP is small energy loss and no background.
Hayakawa model’s position resolution is bad.
B-field improve position resolution in GANIL model.
Concept design using femm and simulate using octave.
Add B-field in obtained result.
3-dimension simulation with MAFIA.