## Slide 1: Precision Measurement of a Prototype Neutron detector for the Future LAMPS Experiment in KoRIA
이기수*, 베나드, 이경세, 홍병식
Korea University
Nuclear Physics Laboratory

## Slide 2: Contents
1. Introduction
2. Pulse analysis using 60Co
3. TOF measurement of neutrons and gamma rays using 252Cf
4. Conclusions

## Slide 3: 1. Introductions
KoRIA(Korea Rare Isotope Accelerator)
- A future multipurpose accelerator for the basic and applied sciences
LAMPS(Large Acceptance Multi-Purpose Spectrometer)
- primary purpose->nuclear symmetry energy
- versatile for nuclear structure and nuclear astrophysics
Neutron detector
- In RI Heavy-Ion collision n/p ratio is important for Symmetry energy
- designed for neutrons of 10 < En < 400 MeV

## Slide 4: LAMPS
x

## Slide 5: LAMPS neutron detector
scintillator
Light Guide
PMT
Lattice of 10 layers
20 module for 1 layer
2m length 1010 cm2 scintillator for 1 module
Detect 10 < En < 400 MeV
Veto counter is placed in front of the neutron detector
JKPS. Vol. 58 No. 2 B. Hong
GEANT4

## Slide 6: Signal process of neutrons in plastic scintillators
n-p elastic scattering
n-12C elastic scattering
n+p->d+γ (neutron capture, Eγ = 2.23 MeV)
n+12C->13C+γ (neutron capture, Eγ = 1.2, 3.6, 4.9 MeV)
Dominant process for signals
-Neutron capture for low energy neutrons
-n-p elastic scattering for high energy neutrons

## Slide 7: VTD&CFD
Voltage Threshold Discriminator
Cut by absolute voltage limit
Constant Fraction Discriminator
Cut by voltage for defined time
C.A.E.N. Mod. N844
C.A.E.N. Mod. N415A

## Slide 8: Condition
Amp.10
C.A.E.N. Mod. N412
Amp.10
C.A.E.N. Mod. N412
Disc.
Disc.
Disc.
C.A.E.N. Mod.
N844
OR
LeCroy 365AL
AND
LeCroy 365AL
Gate
ADC
LeCroy 2249A
ch1
ch2
Common start
TDC
LeCroy 2228A
stop
Right
detector
Left
Trigger
BC-408 disc
Coincidence measurement
- Threshold for signal: 140 mV
- Threshold for trigger: 20 mV

## Slide 9: 2. Pulse analysis using 60Co
60Co
60Co emits back-to-back γ with energy 1.17, 1.33 MeV
Determine position using time difference of each side
Measurement carried out moving each 10 cm from left side
60Co

## Slide 10: Time difference of each position
Time peak moves along position

## Slide 11
Resolution: 0.24 cm
Resolution: 0.2 cm
Position resolution

## Slide 12: ADC attenuation

## Slide 13
ADC ratio

## Slide 14: Compton edges
Compton edge of γ from 60Co: 1.04 MeV
VTD
Compton edge: 120, 110
Threshold: 80, 50-> 347 , 236 keV
CFD
Compton edge: 140, 135
Threshold: 90, 90-> 334, 347 keV

## Slide 15
Time Walk Correction

## Slide 16
Time Walk Correction

## Slide 17: 3. TOF measurement of neutrons and gamma rays using a 252Cf
252Cf
1.0 m
Trigger | Detector
γ | γ
n | γ
γ | n
n | n
- 252Cf fission emits γ and n
- Some combination of signals exist
- 1 m distance is not enough to separate 4 combination
Notes: Gate 55ns

## Slide 18
Time-Of-Flight distributions for γ and n
Neutron region: 19~42 ns
Neutron region: 17~44 ns
γ
n
n
γ

## Slide 19: Fission neutrons from 252Cf and Watt spectrum
Physical Review (108) 411
96.9% α decay+3.1% fission decays
Neutron energy: 0.04~15 MeV
Mean neutron energy: 1.7 MeV
Average number of neutrons per fission: 3.76
Mean gamma energy 0.87 MeV
Average number of γ per fission: 8
80%
20%

## Slide 20: ADC for energy
Linear dependence in energy and ADC
Minimum and maximum energy are not linear

## Slide 21
Resolution of 1 trigger: 308 ps
Resolution of VTD: 788 ps
Resolution of CFD: 594 ps
VTD-trigger: 725 ps
CFD-trigger: 507 ps
Resolution of one side
VTD: 513 ps
CFD: 359 ps
Trigger resolution

## Slide 22: 5. Conclusions & Future tasks
Conclusions
1. Resolution to determine the hit position: VTD->0.24 cm, CFD->0.2 cm
->important to discriminate multi-hit events
2. Light loss due to attenuation of the light<14%(VTD), <20%(CFD) for the 1 m long detector module
->neutron detector for LAMPS is 2 m long
3. Time Walk Correction reduces resolution
4. Digitization: threshold for electron-equivalent signals~340 keV
5. In this test, neutrons emitted from 252Cf with En>~5 MeV were reliably measured from a TOF method
6. Resolution of one side is 513 ps(VTD), 359 ps(CFD)

## Slide 23: Back Up

## Slide 25: Single detector module for LAMPS neutron detector
scintillator
Light guide
PMT
Bicron BC-408
Decay constant: 2.1 ns
Bulk light attenuation length: 380 cm
Refractive index: 1.58
H:C ratio: 1.104
Density: 1.032
Softening point: 70 ℃\
Arcrylic
Density: 1.18 g/cm3
Refractive index: 1.4914
H2431-50
Wavelength short: 300 nm
Wavelength long: 650 nm
Transit time: 16 ns
Gain: 2.5e+6

## Slide 26: CFD time difference

## Slide 27
Resolution: 0.24 cm
Resolution: 0.2 cm
Position resolution systematic first

## Slide 28
Time Walk Correction

## Slide 29
ADC for energy