## Slide 1
Establishing a Frontier Recoil
Separator in RISP
- Installation/development of CRIB
- New properties for KRS
- Development of research groups

## Slide 2
Experience for CRIB

## Slide 3
Facility Development
- Good design and efficient construction
- Establish research programs
- Continuous system development
- Development of research groups

## Slide 4: CNS Facilities at RIKEN
Ge
CRIB
CNS-BT
CSM
AVF
/HyperECR
/ SuperECR
RIBF
AVF-BT
(Under CNS-RIKEN joint
venture program 2000- )
PA
AVF Upgrade Project

## Slide 5
CRIB Project Outline
1997.4 CNS established. New cyclotron facility planning started.
1997 Design work for a low-energy RI beam facility started.
1999.6 Project proposal submitted to RIKEN
1999.10 Shutdown the SF cyclotron
2000.3 CNS moved to Wako for joint venture with RIKEN
2000 Installation of CRIB to E7 room
2001.2 First Program advisory committee for CRIB
2001 First beam to the production target
2001 Installation of Wien Filter
Installation of a window-less gas production target
2001 Installation of flat-top acceleration mode for AVF cyclotron
2003 Completion of Wien Filter
2007 Installation of a cryogenic production target
2009 Installation of a non-destructive beam monitor

## Slide 6
year
Confirm
basic design
Technical discussions
w/ Producers
Bidding
start
Production
Confirm
final design
Installation
Producer
decided
Tuning/testing

## Slide 7: Summary of Research Activities at CRIB and the Scope
Outline of CRIB project
CRIB Facility and AVF Upgrade Project
- Ion Source development
- AVF development (E > 10 MeV/u, and H=1, 3, K=45→79)
- Beam line development (optimization + non-destructive
beam monitoring)
- New cryogenic production target
- Wien filter
3. Research Programs at CRIB
- Nuclear Physics
Proton and alpha structures
- Nuclear Astrophysics
(a,p) direct measurements, ANC and Trojan Horse Methods
- Applications
4. Possibilities
2011.6

## Slide 8
AVF Upgrade Project

## Slide 9: Direct Method with RI Beams
RIB intensities reaction type
104 pps  Resonant scattering w/thick target method
eg. 22Mg+p
106 pps  Rearrangement reactions
eg. (a,p), (a,n), (d,p), . . .
108 pps  (p,g), (a,g), . . .
Total system development=AVF Upgrade project
1. Ion source 2. Accelerator
- SuperECR - FT mode, Modify central region
3. Beam transport 4. Production target
5. Separator - Multipole element

## Slide 10
AVF
HyperECR
PA
AVF Upgrade Project
CRIB
+Super ECR
+flat-top
+K=45 => K=79
+New central inflector
+ H=2+(1)
+Cryogenic target
New IS BT
Multi-beam
switcher
Glaser
lens
New CRIB BT

## Slide 11: Under AVF Upgrade Project
● Extensive ion source installation, and development
Two ECR sources, beam switcher, etc.
Many new beam species with high intensities.
● Installation of flat-top mode acceleration ⇒ better quality beam
● Higher beam energies of the primary beams; 6 ⇒ 12 MeV/u
● Higher beam intensities of the primary beams; ⇒ > 1 pmA
● New beam line for CRIB
● Non-destructive primary beam monitor while RI beam
production
● Complete Wien Filter system ⇒ Better purity RI beams
● Cryogenic target ⇒ Achieved 2x108 pps of 7Be
● Low-energy RI beam monitoring ⇒ Introduction of MCP
● Gamma detector array for radiative capture reactions
10 NaI detectors are prepared.
● Active target-detector system(GEM-MSTPC) development
Possibilities;
● Primary beam quality  window-less gas production target
● High quality RI beams
→ Installation of multi-pole elements for aberration correction
● Room background reduction

## Slide 12: Beam dynamics simulation through the AVF cyclotron
Injection line
ESD
De
Magnet sectors
Injection line
ESD
Dee
Magnet sectors
● Optimized the operation mode.
* Tested with N14 beam acceleration.
● Made a best design of the central region of the cyclotron for high efficient acceleration
● Identified the reliable operation scheme. New monitor systems suggested.
2008/04/7 08 CNS Guidance
Sergey B. Vorozhtsov
Notes: 12

## Slide 13
CRIB Facility

## Slide 14: CNS Facilities at RIKEN
Ge
CRIB
CNS-BT
CSM
AVF
/HyperECR
/ SuperECR
RIBF
AVF-BT
(Under CNS-RIKEN joint
venture program)
PA
AVF Upgrade Project

## Slide 15
0 5 m
F2
Degrader
Heavy ion beams of 5-10 MeV/u from AVF
F3
F1
● RIB ~ 103-8 pps at F3
● DE/E ~ 0.5 – 1 %
● Purity ~ 90 - 100 %
A low-energy inflight-type RI Beam
Separator (CRIB)
(±200 KV)
Wien Filter
F0
Cryogenic
Production
target
Achromatic
focal plane
Double
achromatic
analyzer

## Slide 16: RIB intensity to be obtained at CRIB
N
Z
available
2
108
107
106
105
・Production target
・Primary beam intensity
~Ix10 by Cryogenic target
108 pps  direct measurement
of (p,g) reactions
Notes: cross section 2mb  1.5 x 10**8 pps

## Slide 17: Radioactiv Beams produced by CRIB (A<20) - with room temperature target -
Secondary Beam | Primary Beam | Reaction | Target (mg/cm2) | Intensity (1/sec) | Purity
7Be4+ 8.1 A MeV | 7Li3+ 150 pnA | (p,n) | H2 gas (0.67) | 3105 | 100%
10C6+ 6.1 A MeV | 10B4+ 200 pnA | (p,n) | CH4 gas (1.33) | 1.6 105 | 90 %
13N7+ 6.5 A MeV | 13C5+ 500 pnA | (p,n) | H2 gas (0.33) | 2105 | 95 %
14O8+ 6.7 A MeV | 14N6+ 500 pnA | (p,n) | CH4 gas (1.33) | 1.7106 | 80 %
18F9+ 2.7 A MeV | 18O4+ 500 pnA | (p,n) | H2 gas (0.67) | 1.5105 | 98%
11C 3.4 A MeV | 10B4+ 200 pnA | (3He,np) | 3He gas (0.25) | 1.7104 | 17 %
12N 3.9 A MeV | 10B4+ 200 pnA | (3He,n) | 3He gas (0.25) | 2.5103 | 3 %
8Li 6.5 A MeV | 7Li3+ 330 pnA | (d,p) | D2 gas (1.33) | 2105 | 98 %
17N 2.0 A MeV | 18O6+ 750 pnA | (9Be,10B) | Be foil (2.5) | 1105 | 25 %

## Slide 18
Secondary Beam | Primary Beam | Reaction | Target (mg/cm2) | Intensity | Purity
21Na 4.2 A MeV | 20Ne8+ 200 pnA | (3He,np) | 3He gas (0.25) | 2.3104 | 12 % no WF
22Mg 4.6 A MeV | 20Ne8+ 200 pnA | (3He,n) | 3He gas (0.25) | 6.6103 | 3 % no WF
25Al 4.0 A MeV | 24Mg8+ 125 pnA | (3He,np) | 3He gas (0.25) | 1.2104 | 6 % no WF
26Si 4.0 A MeV | 24Mg8+ 125 pnA | (3He,n) | 3He gas (0.25) | 3103 | 1.5 % no WF
23Mg 4.0 A MeV | 24Mg8+ 125 pnA | (d,t) | D2 gas (0.33) | 3.2 104 | 12 % no WF
39Ar15+ 4.0 A MeV | 40Ar11+ 120 pnA | (3He,a) | 3He gas (1.0) | 3.2 104 | 20 %
Radioactiv Beams produced by CRIB (A>20) - with room temperature target -
Notes: 3x4=12

## Slide 19: Re-circulation cryogenic production target
Features:
Lq. N2 cooling (automatic refill)
for the better cooling power (<100 W) and thicker target.
Forced target gas flow (100 l/min) to have a better cooling and to avoid local density reduction by the beam.
Oxygen density monitor in the gas system.
Hydrogen room sensor.
H2 target cooled by
liquid Nitrigen
7Be ~ 2x108 achieved !
with 1.8 pmA
Flow ≦100 lit/min.
RI beam
Target durability ~ x 3-4 Gas target density ~x 3
~ x 10 intensity increase

## Slide 20: Circulation recovers the density loss
7Beproduction rate
with 1.4 pmA
Gas circulation recovers
the density loss
density
loss !
Recovery
Same problem for plasma target !  fast flow target

## Slide 21
CRIB Machine Times Accepted
year | number of programs | allocated days
2001 | 3 | 19
2002 | 6 | 35
2003 | 7 | 37
2004 | 4 | 18
2005 | 8 | 59
2006 | 6 | 47
2007 | 2 | 6.5
2008 | 8 | 50.5
2009 | 3 | 22
2010 | 4 | 52
SUM | 51 | 346
* Commisioning and facility test times are not included.

## Slide 22: 21Na(a, p) reaction

## Slide 23: Early Stage of rp-Process
ap-process
Targets of
nuclear g-ray
observation
Cycle;
4H→4He+Q
rp-process
?
？

## Slide 24
6.2 MeV/u
20Ne(d,n)21Na in inverse kinematics
Beam production
21Na beam
Energy:
39.5 ± 0.9 MeV
Purity:
83 – 95 %
Intensity:
~ 5x105 pps
Slit
Purity > 90 %
Purity < 10 %
PPAC < 106 pps

## Slide 25
a+21Na
p+24Mg
25Al
(x1,y1)
(x2,y2)
(x3,y3)
(x4,y4)
Physics Problem and Exp. setup
x
Binh

## Slide 26: 21Na(a,p) Study
QL=0-5o
QL=5-10o
21Na(a,po) 24Mg
(Gruhle, NPA286)
21Na+a
resonant
elastic
scattering
Preliminary
Notes: NPA286, 523, 1977

## Slide 27
Er (MeV) | Гα(MeV) | Jπ | l
4.077 | 0.1487 | 3/2- | 3
4.337 | 0.2779 | 5/2- | 3
5.162 | 0.7393 | 7/2+ | 2
5.721 | 0.4356 | 3/2+ | 2
R-Matrix Analysis
Resonance Parameters
4.08
4.34 5.16 5.72
q=0-5o
q=5-10o
Preliminary

## Slide 28
R-matrix analysis on 21Na(a,a)
a Reduced Width/
Wigner limit
a-cluster
resonances !

## Slide 29
Transitions to
high-lying states
in 24Mg
(Ex(25Al)-Q(a))
Transition strengths of 21Na(a,p)24Mg
(a,p0)
Present rate
includes
only (a,p0)

## Slide 30
21Na(a,p)24Mg Reaction Cross Sections
Non-Smoker
(a,p0) data
(from time rev.)
Direct
measurement
Calculated
(from a-scatt.)
Large
enhancement !

## Slide 31
S-(present) / S(NACRE)
Ecm(MeV)
T(GK)
Present 21Na(a,p)
NACRE; 21Na(a,p)
(accepted presently)
D’Auria; 21Na(p,g)
S-(present) / S(NACRE)
Ecm(MeV)
21Na
22Na
22Mg
23Mg
Ignition temperature a half ?
Scenario pathway is wrong ?
Reaction rate of 21Na(a,p)24Mg
ap-process
wrong? !

## Slide 33: Levels for 21Na(a,p)
25Al
Present
25Al
References
25Mg
References
Notes: Ga primarily decides the r.r.

## Slide 34
Application Programs
at CRIB

## Slide 35
1) Production of Polarized Radioactive Beams via The Inverse-
kinematics Reactions and Their Application
(K. Asahi/TIT)
2) Environmental dependence on the half-life of nuclei
(T. Otsuki/Tohoku Univ.)
3) Detector development for RIBF experiment
(Sumikama/Tokyo University of Science, and
S. Nishimura/RIKEN)
→ Successful measurements of r-process nuclei (PRL, 2011)
Application programs

## Slide 36: Physics with Spin-Polarized Beam and b-NMR
Nuclear Physics
  Nuclear moments measurement
Condensed Matter Physics
  Probe of behavior of impurity implanted into semiconductor
  Goal: research behavior of nitrogen implanted into diamond
mN
mN
Asahi Group
12B
12B
Si
C
e
Asahi

## Slide 37: 17N b-NMR Spectrum
Ab Q = -0.57
B0=7.0771 kG
MgO stopper

## Slide 38
Otsuki

## Slide 40
Possibilities at CRIB

## Slide 41: Direct Method with RI Beams
RIB intensities reaction type
104 pps  Resonant scattering w/thick target method
eg. 22Mg+p
106 pps  Rearrangement reactions
eg. (a,p), (a,n), (d,p), . . .
108 pps  (p,g), (a,g), . . .
Total system development=AVF Upgrade project
1. Ion source 2. Accelerator
- SuperECR - FT mode, Modify central region
3. Beam transport 4. Production target
5. Separator - Multipole element

## Slide 42
Nuclide | 46Cr | 46V | 45Ti | 46Ti | 43Sc | 36Ar
Purity(%) | 2 | 9 | 2 | 16 | 5 | 51
Rate(pps) | 6 | 27 | 7 | 49 | 14 | 157
Half life | 260ms | 422.4ms | 184.8min | stable | 3.891h | stable
46Cr17+
(2%, 7pps)
@80pnA
Figure of PI at F3
RI beam of A=40-50 production by
a fusion reaction of 12C+36Ar at 3.6 MeV/u
Clean particle
separation !
Wakabayashi

## Slide 43
Primary beam quality
Production target; window-less→ x10
Secondary beam quality; size→ 1/2
Wien filter transmission; 30→ > 80%
RI beams of A > 40
Beams of fission fragments; very high intensity
Background for gamma spectroscopy;
→ in beam g-spectroscopy
8. Active target → versatile for many type
reaction studies
Possibilities for the CRIB facility
Notes: Emittance ?

## Slide 44: High T rp-Process
14O(a,p)17F
(e.g. X-ray burst, SNe)
13N(p,g)14O
18F(p,a)15O
(p,g) + (a,p), (a,g)
Teranishi
Notani, Hahn
He,
Hahimoto

## Slide 45
Only the first and second T=3/2 levels are well known experimentally.
T=3/2 levels in A=9 nuclei
Energy systematics of isobaric multiplets (Thomas-Ehrman shift)
structure of 9Li and its analog
Jp and G
Teranishi

## Slide 46
Complete (a,p) studies – done only for high T
Direct measurement of (p,g) and (a,g)
a-cluster structures in unstable nuclei
Particle structure in unstable nuclear region
- isobaric analog states (Teranishi)
5. Physics with RI beams of A = 40-60
6. Physics with spin polarized beams
7. Physics with fission fragments
8. . . .
Possibilities of Physics at CRIB
Notes: Emittance ?

## Slide 47
International Collaborations
RIKEN
Kyushu University
Tohoku University
Osaka University
Tsukuba University
Yamagata University
KEK
Tokyo I. T.
Kyoto University
+ Others
Chung Ang University
Ewha Womans University
Seoul National University
CIAE, Beijing
IMP, Lanzhou
IOP, Vietnam
University of McMaster
Michigan State University
ATOMKI, Hungary
IOP, Orsay
INFN, Catania
University of Padova
University of Edinburgh
University Sao Paulo
Thanks for all
for supporting CRIB
and collaborations

## Slide 48
Nuclear Physics Experiments at KRS
Direct reaction study of stable/unstable nuclei
2. Resonant scattering
Elastic, rearrangement, capture
Fusion/ Fission product spectroscopy
with in-beam spectroscopy
Rare event study
5. New research domains
Priority setup for KRS project
Subjects, group
Group
Time line of research activities and of building the groups
We need to determine the basic functions;
RIB production – degrader, WF
Large acceptance for in-beam spectroscopy - two stage,
large bite
High resolution particle spectroscopy – large p dispersion
Polarized RIB – rotatable stage
Fission fragment spectroscopy ? - GARIS mode,

## Slide 49
Establish an Extensive Inflight separators
at low energies
1. Primary beams
- Ion Source – intensity, species, emittance,
- Accelerator – efficiency, emittance, flat-top mode,
- beam line – efficiency, square beams, emittance aperture
2. Production target – window-less prod. target w/fast flow
or plasma window target
– production reactions and yields
3. Separator
- basic property – production/reaction scheme
for capture reactions, fusion/fission residues,
angular acceptance,
– high-resolution spectrometer use, etc.
– room separation (room background)
- efficiency, acceptance, non-zero degree producntion (pol. RIB).
- purity – Wien filter or RF deflector, parallel degrader
- RI beam property – small spot size, parallel beam
(higher order aberration)
- RI beam monitor – fast, high eff. counter (PPAC, diamond, ..)
4. Experimental target/ detectors

## Slide 50
2014
2015
2016
2017
2018
2012
2013
RISP construction
SCL1 or SCL3 (18.5 MeV/u)
Recoil spectrometer
Construction/tuning
ISOL
SIB/RIB exp.
RIB exp.
Cyclotron installation
RIB exp. @other labs.
Final design
Discussion/
Producers
bidding
Building construction
Basic design
Notes: See 11/1 2012 mail from Kwon

## Slide 51
Construction work
Detailed drawings
Manufacturing
Setting
Separator
Wien Filter
Production target
Control system
Company A
Company C
Company B
Company A
In-house persons

## Slide 52
Nuclear Physics Experiments at KRS
Direct reaction study of stable/unstable nuclei
2. Resonant scattering
Elastic, rearrangement, capture
Fusion/ Fission product spectroscopy
with in-beam spectroscopy
Rare event study
5. New research domains
Priority setup for KRS project
Subjects, group
Group
Time line of research activities and of building the groups
We need to determine the basic functions;
RIB production – degrader, WF
Large acceptance for in-beam spectroscopy - two stage,
large bite
High resolution particle spectroscopy – large p dispersion
Polarized RIB – rotatable stage
Fission fragment spectroscopy ? - GARIS mode,
Need design study
till 2013 February

## Slide 53
If possible, concentrate the efforts
on the low energy part.
↑
Research output
Man-power

## Slide 56
present
Confirm
basic design
Technical discussions
w/ Producers
Bidding
Production
Confirm
final design
Installation
Producer
decided
Tuning/testing

## Slide 57: Summary of Research Activities at CRIB and the Scope
Outline of CRIB project
CRIB Facility and AVF Upgrade Project
3. Research Programs at CRIB
4. Possibilities
2011.6

## Slide 58
Make a nuclear astrophysics physics forum in the pacific rim
based on CRIB, pelletron in Hanoi, KoRia, ….
● Exchange information and ideas
● Make collaboration works
● Make a symposium
● Enhance the nuclear astrophyscs activities in the area

## Slide 60
21Na(a,p)24Mg Reaction Cross Sections

## Slide 61: 21Na(a,p) Study
QL=0-5o
QL=5-10o
21Na(a,po) 24Mg
(Gruhle, NPA286)
21Na(a,a)
Preliminary
Le/CRIB coll.
Notes: NPA286, 523, 1977