## Slide 1
Symmetry energy 연구용
대면적 스펙트로미터
(Large Acceptance Multipurpose Spectrometer, LAMPS) 설계
고려대학교 이경세

## Slide 2
위탁 세부과제 목표
고에너지용 실험 (최대 250 AMeV) 및
낮은 에너지 (~ 20 MeV) Day-1 physics 실험용 장치 상세 설계
중성자 섬광검출기 (neutron array detector) (고려대)
중성자 검출기 performance 시뮬레이션 (GEANT4)
중성자 검출기 prototype detector test
2. Time Project Chamber (고려대/부산대)
GEM-TPC simulation
GEM prototype detector
DAQ 및 검출기 electronics (부산대)
LAMPS DAQ system 설계
GEM-TPC electronics
4. 낮은 에너지 physics simulation (전북대)

## Slide 3
LAMPS detector project
1. High-energy, high-intensity neutron-rich RI beams
Neutron-rich RI beams (ex. 132Sn, 142Xe) at maximum ~250 AMeV up to ~ 106 pps
Low-energy detector system for Day-1 experiments
Symm. Energy and PDR/GDR with ~ 20 AMeV
Physics motivations
Equation of state (EOS) of neutron-rich nuclear matter at low & high density up to ρ ~ 2ρ0
1. Probing Esym of neutron-rich matters at a wide range of density from neutron-rich HI collisions
2. Understanding astronomical phenomena in neutron stars, and super novae by the EOS of nuclear matter at high density
3. Nuclear synthesis
4. Exotic nuclei lying near neutron drip lines

## Slide 4
Symmetry Energy 연구
Nuclear Equation Of State (EOS) of nuclear matter in the isospin space
symmetry energy
Energy in symmetric matter
Energy per nucleon
ρn : neutron density
ρp : proton density
ρ0 : Saturation density
Nucleon density ρ=ρn+ρp
ρ=ρn+ρp
0
density
Symmetric matter
ρn=ρp
δ
???
PRC 64, 034314 (2001)

## Slide 5
LAND/ALADIN: slope parameter,
L between 30 ~ 60 MeV for 132Sn

## Slide 6
LAMPS for Symm.E
with ~ max 250-AMeV
132Sn, 142Xe, and stable HI …
TOF array
Neutron calorimeter
TPC
Target system
Silicon-strip tracker
Solenoid magnet
Super-conducting dipole magnet
Beam
monitoring
system
Tracking chambers
He bag
Vacuum
LAMPS for High-energy
Experiments (conceptual)
Solenoid magnet
+ TPC
+ silicon-strip tracker
Dipole magnet
+ tracking chambers
+ TOF array
Neutron calorimeter at +- 8o
~ 3 π Sr
~ 30 mSr
50 mSr

## Slide 7
1. Design of experimental setup
For low energy (Ebeam < 20 MeV/u)
For high energy (Ebeam > 20 MeV/u)
2. Optics calculation for dipole magnet (고에너지 실험)
Rotatable dipole magnet and focal plane
3. Detector simulation and R&D
TPC (~ 8 Sr acceptance)  위탁과제
E-E (Si+CsI)  위탁과제
Focal plane detector system
(dipole spectrometer, 고에너지 실험)
Focal plane ToF
(t < 100 ps for p/p<10-3 at =0.5)
Neutron Wall  위탁과제
(capable for neutron tracking)
Gamma/charged-particle array
(Pigmy/Giant dipole resonance)
Performance at RISP (김영진)

## Slide 8
TPC in a solenoid magnet @ 1 T
- Acceptance ~ 8 Sr for π+, π-, p, n, d, t, 3He, 4He and fragments up to 7Li
TPC capable of measuring from MIP (π- and π+) to fragments.
Cylindrical TPC

## Slide 9
Electronics Flange
Simulations GEM-TPC
Triple GEM amplication
Gas: 70% Ar + 30% CO2
Maximum drift length: 60 cm
Readout pads ~ 90 k (2.5 mm hexagonal pads)
~ 22 k (5.0 mm hexagonal pads)
Charge for MIPs ~ 160 pC
Digi. threshold ~ 100 pC
Gain with a
single GEM
Dispersion

## Slide 10
2mm-hex pads
5 mm-hex pads

## Slide 11
Current planned hardware R&Ds for TPC
GEM Detector
1) Procurement of six 10 x 10 cm2 GEM foils (KU)
Design of Triple-GEM detector hex pads (PNU and KU)
Electronics
1) Procurement of 256-channel FEE s (including ASIC chips) from GET collaboration (PNU and IBS)
DAQ design (PNU)
Electronics for Level-1 triggers for individual detectors
Global trigger electronics and DAQ

## Slide 12
H-type Dipole
Pole size (x,z) : (150 cm, 100 cm)
Maximum By = 1.5 T
Gradient : 0.5 T∙m < ∫ By dz < 1.5 T∙m
Solenoid
Size (r,z) : (50 cm, 200 cm)
Maximum Bz ~ 1.0 T
Solenoid and dipole magnets in the original conceptual designs

## Slide 13
Magnet designs
Simulation for dipole magnets for a QD system (KU and IBS)
Other options for a QD system

## Slide 14
Milestones
1) Considering various designs
Not just D or QD,
but QQD, QQDD, QDD etc.
2) More precise simulation
Needs GICOSY with Geant4 to solenoid effect for low-energy particles
QQD system
QDD system

## Slide 15
Silicon-CsI array in beam-pipe region
Coverage: 1.6 < η < 2.1
Identification of particles with Z=9
Silicon layers: 100 + 400 + 400 μm
CsI blocks: trapezoidal with a 10-cm depth

## Slide 16
Measurement of energies with particle identifications

## Slide 17
Sector division in a Si-CsI ring
1) A reliable occupancy per pixel ~ 0.1
2) 16 channels for a single module
3) Total number CsI channels in a ring = 8 x 16 = 128

## Slide 18
Neutron detector for high-energy experiment

## Slide 20
Prototype detector module
1) PMT readout at both ends of 100-cm bar
2) Time resolution for (tR + tL)/2 ~ 500 ps
3) Position resolution for tR – tL ~ 5 cm

## Slide 22
New Hardware R&D (KU and IBS) for low-energy experiments
Super module for neutron detection system for low-energy experiments
1) A super model Composed of 9 plastic blocks
Ordered 15 plastic blocks (Rexon) and 20 light guides
Planned to perform beam tests
Measurable neutron energy ~ 1 MeV
Target
Gamma & charged
particle detector array
Beam

## Slide 23
Current Status & Milestones
목표: 고에너지용 실험 (최대 250 AMeV) 및 낮은 에너지 (~ 20 MeV) Day-1 physics 실험용 장치 상세 설계 완료
현재까지 완료된 연구 내용
1. 중성자검출기
IQMD/GEANT4 활용 고에너지 실험 중성자 검출기 설계
고에너지 실험용 중성자 검출기 prototype detector 및 실험
2. TPC/Si-CsI
Triple GEM simulation (GEANT4)
Si-CsI array (GEANT4)
DAQ 및 검출기 electronics
LAMPS DAQ system 설계
GEM-TPC electronics
4. 고에너지 실험 LAMPS spectrometer 기초 설계
Dipole magnet (D, QD systems)
5. 낮은 에너지 physics simulation
IQMD/GEANT4 활용 Si/CsI array data performance 도출

## Slide 24
향후 3개월 간 수행할 연구 내용
1. 중성자검출기
IQMD/Gemini/GEANT4 활용 낮은 에너지 실험 중성자 검출기 설계
낮은 에너지 실험용 중성자 검출기 super module prototype detector 제작
252Cf 및 양성자 빔 활용 실험
Multi-hit 분석 알고리즘 개발
2. Time Project Chamber
시뮬레이션을 통한 TPC 용 Triple GEM prototype 구조 설계
DAQ 및 검출기 electronics
LAMPS DAQ prototype 구축
GEM-TPC electronics 발주
4. 고에너지 실험 LAMPS spectrometer 상세 설계 완성
Solenoid magnet (field map simulation)
Dipole magnet (D or QD → QQD, QDD, or QQDD)
5. 낮은 에너지 physics simulation
IQMD/GEMINI/GEANT4 활용 낮은 에너지 실험 event generation 및 data performance simulation