## Slide 1
Status of PHENIX RPCs at Run 13
C. Kim1, * B. Hong1, Eunah Joo1,
and PHENIX Forward Upgrade Group2
1 Department of Physics and Korea Detector Laboratory, Korea University, Seoul 136-713
2Brookhaven National Laboratory, New York 11973
for the PHENIX collaboration

## Slide 2: Outline
Introduction
  RHIC and PHENIX
  W physics
  PHENIX Run 13
PHENIX RPCs
  Overview
  Production, QA, and Installation
  Status at Run 13
Summary and Perspectives

## Slide 3: 1. Introduction - a. RHIC and PHENIX
PHENIX
STAR
PHOBOS
BRAHMS
RHIC (Relativistic Heavy-Ion Collider) at BNL, NY, US:
    Max. √sNN : 510 GeV (pp) / 200 GeV (AA)
    Max. luminosity: 1.5 × 1032 cm−2 s−1 (pp) / 2 × 1026 cm−2 s−1 (AA)
    The only machine capable of colliding high-energy polarized proton beams
PHENIX (Pioneering High-Energy Nuclear Interactions eXperiment):
    One of the two ongoing physics experiments at RHIC
    Goal: Discover and examine the QGP & Analyze the proton spin

## Slide 4: 1. Introduction - a. RHIC and PHENIX
PHENIX detector

## Slide 5: 1. Introduction - b. W physics
Spin crisis:
    DIS result at 1980s: proton spin is not a simple sum of its constituent quarks
    Component-by-component approach:
    quarks/antiquarks, gluons, and their angular momenta
    → ½ = ½ΔΣ + ΔG + Lz
W measurement at PHENIX:
    Full flavor separation of quarks/antiquarks
    Measure the polarization of the quark by leptons decayed from W boson
ALW: single spin asymmetry
p: beam polarization (Max. 70 % for 510 GeV pp)
NL(R)(W) : # of events contains the muons from W
with corresponding helicity (L or R)
ΔΣ = 0.366 ± 0.017
for Q2 = 10 and 0.001 ≤ x ≤ 1

## Slide 6: 1. Introduction - c. PHENIX Run 13
PHENIX Run 13 - focused Run for the W measurement
    Major updates from Run 12: RPC1 integrated to trigger, FVTX data available

## Slide 7: 1. Introduction - c. PHENIX Run 13
 | Goal (total) | Run 11 | Run 12
L (pb-1) | 300 | 17 | 30
P (%) | 55 | 51 | 56
 | Goal (total) | Current (4/15) | Target
L (pb-1) | 300 | ~ 40 | 250
P (%) | 55 | ~ 50 | 55
Achieved (Run 11/12)
Run 13

## Slide 8: 2. PHENIX RPCs - a. Overview
PHENIX forward muon trigger upgrade for W program
  35 cm SS310 (Stainless Steel) absorber: reduce low-p hadron’s punch through
  MuTRG: fast determination of high momentum tracks (tracking)
  RPC: provide timing information and rough position information (timing + tracking)
MuTRG
RPC 3
RPC 3
RPC 1
  SS310 (35 cm) absorber

## Slide 9: 2. PHENIX RPCs - a. Overview
Momentum selectivity through online sagitta measurement
    Uses MuTr station 1, 2, 3 and RPC station 1, 3
    Implement trigger using fast, parallel logic on FPGA’s
    Beam related background rejected by RPC’s timing information
RPC 1
RPC 3
  SS310 (35 cm) absorber

## Slide 10: 2. PHENIX RPCs - a. Overview
η acceptance of RPCs
(side view)
155.75
908.05
483.3
361.0
264.1
141.6
376.1
252.2
RPC3
~ 40
~ 105
RPC1
~ 64
1.185
2.069
1.388
1.653
1.615
1.993
1.949
2.557
Beam pipe
Run 12
Run 13
Update in Run 13 trigger configuration: RPC1 integrated to the DAQ during Run 12

## Slide 11: 2. PHENIX RPCs - a. Overview
PHENIX muon trigger RPC
    Bakelite double gap RPC
    Based on CMS endcap RPC technology and expertise
    Fast time response: 1 ~ 2 ns for MIP
    Gas mixture:
      95 % C2H2F4 (R134A, base gas for avalanche mode RPC)
      4.5 % i-C4H10 (isobutane, photon quencher)
      0.5 % SF6 (electron quencher)
      ~ 40 % relative humidity
Cu foil (2 mm)
Mylar sheet
Module frame (Al)
PHENIX RPC requirements Most conditions are same as those for the CMS endcap RPCs | 
Time resolution | ≤ 3 ns
Average cluster size | ≤ 2 strips
Efficiency | ＞ 95 %
Rate capability | 0.5 kHz/cm2
Average noise rate | ＜10 Hz/cm2
# of streamer mode | ＜10 %

## Slide 12: 2. PHENIX RPCs - b. Production, QA, and Installation
Module assembly flow
Lay down a Mylar sheet & Cu foil
on the bottom module frame
Put lower gap &
Attach service lines (HV, gas)
Prepare readout strips &
Place it on the lower gap
Put upper gap on the strip &
Attach service lines
Put a Mylar sheet on upper gap &
Wrap the cu foil
Close module frame
Modules for the station 3: ALL (total 96) modules were produced
Fully assembled RPC detector module
Before wrap the Cu foil
Connect CPE cable to the H.V cable (upper gap)
Connect gas tubes to the upper gap
Put upper gap on the readout strip
Put readout strip on the lower gap
Preparing readout strip (attach signal cables)
Connect CPE cable to H.V cable on the bottom RPC gap
Connected gas tube
Place lower gap into Cu foil & Connect Polyethylene gas tubes
Lay down Cu foil on the Mylar sheet (+ frame)
Assembly of module 3C
Module frame (Al)
2 mm Cu foil
Cu readout strip
Gap

## Slide 13: 2. PHENIX RPCs - b. Production, QA, and Installation

## Slide 14: 2. PHENIX RPCs - b. Production, QA, and Installation
Module QA
Before assembly
(Gap QA)
Spacer pop check
Gas leakage check
HV hold
Dark current
After assembly
(module QA)
Noise rate check
Cosmic ray test
QA (Quality Assurance) for a detector module:
    Before assembly: spacer condition, gas leakage, HV hold and dark current
    After assembly (test by cosmic muons):
    noise rate, total & strip efficiency, time resolution & cluster size
RPC cosmic ray test stand - event display
cosmic ray
trigger scintillators
RPC readout strip
planes
cosmic ray trajectory

## Slide 15: 2. PHENIX RPCs - b. Production, QA, and Installation
Noise rate:
RPC HV = 9.5 kV, PHENIX RPC FEE threshold = 160 mV
Noise rate (Hz/cm2)
Raw TDC :
1 unit = 100 ns/44 = 2.41 ns
Time resolution vs. HV
Efficiency of a module (%) vs. HV
with different threshold
Cluster size of a module vs. HV
with different threshold
Operation voltage
Operation voltage
PHENIX requirements
PHENIX requirements
Module QA results

## Slide 16: 2. PHENIX RPCs - b. Production, QA, and Installation
Station 3 (16 half octants)
A half octant (3 RPC modules)
RPC3
Module C
Module B
Module A
2.05 m
4.93 m
0.54 m
RPC station 3
    One side (N or S) of RPC station 3 is composed of 16 half octants
    A half octant is composed of 3 RPC modules (type A, B, and C)
    Each module is a double-gap RPC which satisfies PHENIX requirements
RPC 3
RPC 3

## Slide 17: 2. PHENIX RPCs - b. Production, QA, and Installation
RPC3N - installation (Nov. 11th, 2009)
RPC3S - installation (Sep. 22nd , 2010)
Fully integrated to the PHENIX DAQ system during Run 11

## Slide 18: 2. PHENIX RPCs - b. Production, QA, and Installation
RPC1
90 cm
67 cm
Octant
34 cm
RPC station 1
    Composed of 16 octants for both sides (8 octants per side)
    Each octant is a double-gap RPC
RPC 1

## Slide 19: 2. PHENIX RPCs - b. Production, QA, and Installation
RPC1N - installation (Sep. 22nd , 2011)
RPC1S - installation (Dec. 07th , 2011)

## Slide 20: 2. PHENIX RPCs - b. Production, QA, and Installation
Hodoscopes for absolute efficiency measurement
RPC3
MuID
MuTR
Hodoscope
Design
Location on the rear side of RPC Station 3

## Slide 21: 2. PHENIX RPCs - c. Status at Run 13
Rpc3DCA
μ
(extrapolated)
MuTR
Muon Track Associated Hit
Raw TDC of RPC
TDC (106 ns for 44 bins)
Count
εrelative =
# of μ tracks w/ RpcDCA cut
# of μ tracks
* only very basic cut are applied in following
efficiency/TDC histograms (next pages)
Efficiency (ε)
TDC peak timing (t)
* The numerator in efficiency definition
corresponds to Muon Track Associated Hit

## Slide 22: 2. PHENIX RPCs - c. Status at Run 13
Sample efficiency for Run 391471 (Apr 15)
    Height dependence observed: vary from side and module type
    Optimization is still ongoing
  * Please note this is QA-purpose online production figures for a Run: NOT even fast production data!

## Slide 23: 2. PHENIX RPCs - c. Status at Run 13
S_1B
S_1C
S_H
S_3A
S_3B
S_3C
N_1B
N_1C
N_H
N_3A
N_3B
N_3C
S_1B
S_1C
S_H
S_3A
S_3B
S_3C
N_1B
N_1C
N_H
N_3A
N_3B
N_3C
Sample timing distributions for Run 391471 (Apr 15)
    All octants/HO structures merged for the quick check
    Both merged/separated case shows beam-related hit timing very well

## Slide 24: 2. PHENIX RPCs - c. Status at Run 13
Sample vs. Time (date) histograms near Run 391471 (Apr 15)
    Peak timing is almost fixed: still got a peak in range even if timing shift occurred
    Most of efficiencies also fixed within resonable range

## Slide 25: 3. Summary and Perspectives
Summary:
    PHENIX RPCs are fully integrated to the PHENIX forward trigger system
    Run 13: dedicated Run for the PHENIX W program
      Integrated L goal for the Run: 250 pb-1
      P goal for the Run: 55 %
      Major difference from Run 12:
      RPC1 integration to the trigger → significant improvement in rejection power
Perspectives:
    Further optimization is still ongoing

## Slide 26: Backup
Muon
Hadron
Muon Tracker
(MuTr)
Muon ID
(MuID)
PHENIX muon arms (before upgrade)
Acceptance
- 1.2 < |η| < 2.2
- Δφ = 2π
Muon Tracker (MuTR)
  - 3 stations of CSCs
Muon ID (MuID)
  - 5 gaps of larocci tube in x & y directions
  - Total 80 cm thick steel absorber (plates)
Muon tracking and triggering
- Tracking by hit positions from each station
- Most hadrons are absorbed before
reaching last gap of the MuID
- Current 1st level rejection factor (RF):
~ 100 (MuID based 1st level trigger)

## Slide 27: Backup
Simulated muons into Muon Arms
(2000 pb-1, with PYTHIA 5.7)
MuID base trigger
(before trigger upgrade)
W measurement at PHENIX muon arms
√s = 500 GeV
σ = 60 mb
L = 1.5 x 1032 cm-2s-1
→ 3.0 x 1032 cm-2s-1 (after luminosity upgrade)
Total interaction rate: 9 MHz
DAQ limit: 2 kHz
Required 1st level rejection factor (RF): 4500
Dedicated trigger system is required:
→ Forward muon trigger upgrade
After trigger
upgrade

## Slide 28: Backup
MuTRG
ADTX
MuTRG
MRG
Level 1
Trigger
Board
MuTr
FEE
Resistive Plate Chamber
(RPC) (Φ segmented)
B
2 planes
5%
95%
Trigger
Trigger
Trigger
Interaction Region
Rack Room
Optical
1.2Gbps
Amp/Discri.
Transmit
Data
Merge
MuTRG
RPC
FEE
Trigger events with straight track
(e.g. Dstrip <= 1)
RPC / MuTRG data are
also recorded on disk

## Slide 29: Backup

## Slide 30: Backup