## Slide 1
FOUR-GAP PHENOLIC RPC’S TEST RESULT WITH
COSMIC MUONS AND HIGH-RATE GAMMAS
Benard Mulilo, Byungsik Hong, Chong Kim, Eunah Joo, Genie Jhang, Hyuncheol Kim, Kisoo Lee, Kwang-Souk Sim, Kyongsei Lee1,
Mihee Jo, Park Sung Keun1,Seung Su Shin, Shin Young Kim1, Songkyo Lee, Suhyun Lee,3, Yeonju Go2,3,4
1Korea University, 2Nuclear and High Energy Physics Laboratory
ABSTRACT
Development of an oiled four gap Phenolic RPC for for use as high-rate particle in high energy physics experiments.
REFERENCE
ELECTRONICS SETUP
CMS collection, Detector performance and software? Technical design report Volume 1, CERN-LHCC 2006-001 (2006)
CMS collaboration, The Muon project, technical design report, CERN-LHCC-97-032 (1997).
H.C. Kim et al>, Quantitative aging study with intense irradiation tests for the CMS forward RPCs, Nucl. Instrum. Meth. A 533 (2009) 102.
M. Abrescia et al., Study of long-term performance of CMS RPC under irradiation at the CERN GIF, Nucl. Instrum. Meth. A 533 (2004) 102.
S. H. Ahn et al., Characteristics of a double gap resistive plate chamber for the endcap region of CMS/LHC: data vs simulation in avalanche mode, Nucl. Instrum. Meth. A 533 (2004) 32.
For more details, please contact: Prof. Lee Kyongsei, Department of Physics, Korea University; Email: kslee0421@korea.ac.kr
MOTIVATION
Prototype RPC with 4 gaps made from HPL plates has been built.
Detector aims at reducing probability of radiation induced degradation &
Improvement of the detection rate capability.
Properties obtained using muons & gammas from a 200-mCi 137Cs source
INTRODUCTION
(1) Test with Cosmic Muons
(2) Test with High-Rate ϒ’s
202013
 | 2-gap RPCs | 4-gap RPCs
Gap thickness | 2.0 mm | 1.0 mm
Total gap thickness | 4.0 mm | 4.0 mm
<qe>avalanche mode | 2.5 ~ 7 pC | 1.2 ~ 2.5 pC
<qe>at 200V> HV95% | 4.0 pC | 1.4 pC
Type of HPL | Phenol+Mel | Phenol+Mel
Thickness of HPLs | 2.0 mm | 2.0 mm
Resistivity of HPLs | 1 ~ 5 ⅹ1010 Ωcm | ~ 1ⅹ1010 Ωcm
Rate capability | < 2.0 kHz cm-2 | > 3.0 kHz cm-2
PROTOTYPE PANEL-SHAPE 4-GAP RPC FABRICATION
TEST RESULTS
2- & 4-GAP RPC COMPARISON
4-gap RPC fabricated with similar tech. as 2-gap RPCs used in CMS.
Size of muon efficiency plateau ≥ 600V for 4-gap RPCs.
At 200V above HV0.95 , <qe> ~1.25pC with threshold ~150fC.
HV shifts~ 500V at Nγ = 4.5 kHz cm-2 with ρ = 5.0 ⅹ1010 Ωcm
No degradation found at Nγ = 4.5 kHz cm-2
Aging issue:<qe> ~1/3 of 2-mm double gap RPCs.
MILESTONES
QA based R&D for the 4-gap RPC manufacture procedure and parts.
Real-size prototype 4-gap RPCs in the high-η regions (RE1/1, RE2/1, RE3) could be used.
R & D to develop Panel-type multigap RPC using:
Oiled phenolic HPL resistive plates
95% Freon & 5% Iso-Butane Gas Mixture.
With high η covering: 0.9 < |η| < 2.1
SUMMARY
Resistivity, ρ ~ 5.0 ⅹ1010 Ωcm at 20oC
Muon Efficiencies
Efficiencies & mean charges of muons
Efficiencies & mean cluster sizes
Charge distribution of muons
Gamma rates
Muon and gamma efficiencies
Mean cluster size
Gamma rate & mean charge
TDC stops threshold = 9mV.
ADC thresholds in offline mode.
Scintillator signal voltage threshold = 30mV.
Noise data & γ-rays obtained by 1kHz clock trigger using 2GHz pulse generator
Gate width for avalanche pulses (FWHM < 10ns) = 40ns.
Accuracy for avalanche charge for each event = 20~ 60fC.
Triggers->3 plastic scintillators; time resolution~500ps.