## Slide 1
J. Ahn4, B. Hong1, E. Joo1, E. Kim3, H. Kim3, Y. J. Kim2, Y. K. Kim2, Y. J. Ko1, K. S. Lee1, J. W. Lee1, H. Lee4, K. S. Lee1, S. Lee1, B. Mulilo1, T. S. Shin2
1Korea University, Seoul, Korea
2Institute for Basic Science, Daejeon, Korea 3Chonbuk National University, Jeonju, Korea
4Pusan National University, Busan, Korea
Plastic Scintillators for Neutron and Charge Particle Detections for LAMPS Experiments at RAON
Contents
Introductions: LAMPS at RAON
Neutron detectors for high-energy experiments
Neutron detectors for low-energy experiments
TOF detectors in LAMPS solenoid spectrometer
Digitization electronics for neutron and TOF detectors
Summary & milestones

## Slide 2: 1. Introductions: LAMPS at RAON
Large Acceptance Multi-Purpose Spectrometer to maximize the use of nuclear physics researches for neutron-rich nuclei
  Main purpose for Symmetry-Energy research
  Understanding astronomical phenomena in neutron stars, black holes, and super novae by the EOS of nuclear matter at high density
  Pygmy Dipole & Giant Dipole Resonances
  Neutron halos and exotic nuclei lying near neutron drip lines
  2. Conceptual designs of LAMPS
  High-energy experiment (250 AMeV)
  Solenoid spectrometer equipped with a 3π-Sr TPC
  Dipole spectrometer with a focal plane detector system
  Large acceptance of neutron detectors via TOF measurement
  Low-energy experiment (< 20 AMeV)
  Vacuum system equipped with Si-CsI detectors
  Large acceptance of neutron detectors via TOF measurement

## Slide 3: Nuclear Equation of State
18
B.-A. Li, L.-W. Chen &
C.M. Ko, Physics Report,
464, 113 (2008)
ρ
0
Nucleon
density
Isospin
asymmetry
Symmetric
nuclear matter
(ρn=ρp)
δ
E/A (MeV)
r (fm-3)
CDR, FAIR (2001)
F. de Jong & H. Lenske, RPC 57, 3099 (1998)
F. Hofman, C.M. Keil & H. Lenske, PRC 64, 034314 (2001)
δ: asymmetry in p & n

## Slide 4
LAMPS: design for high-energy experiment
Solenoid spectrometer
Solenoid magnet (0.6 ~ 1.5 T)
TPC (∆P/P ~ 10-2)
Si-CsI array (∆E/E ~ 10-2)
Plastic barrel detectors for trigger
Dipole spectrometer
Quadruple-Dipole magnets
(QD or QQD) for focal plane (∆P/P ~ 4 x 10-4)
Drift chambers
TOF wall
Neutron detector array
Acceptance ~ 100 mSr
∆E/E ~ 2 x 10-2

## Slide 5: Magnets in the original designs
H-type dipole
Pole size: (x,z)=(150 cm, 100 cm)
Maximum By: ~ 1.5 T (~ 4 T for SC option)
Gradient: 1.0 T∙m < ∫By∙dz < 2.0 T∙m
Solenoid
Size (r,z) : (50 cm, 200 cm)
Maximum Bz: about 1.0 T
Simulation by S. Hwang & J. K. Ahn

## Slide 6
  TPC
  Gas: P10 or Ar +CO2 mixture
  Drift field: ~ 150 V cm-2
  Read-out: Triple-GEM & hexagonal pads (5 mm) at both endcaps
  Choice of GEMs: higher rate capability from MIPs to heavily ionizing particles
Hexagonal pads
for a prototype

## Slide 7
LAMPS: design for low-energy experiment
Vacuum chamber
Si-CsI array (charged particles & γ)
∆E/E ~ 10-2
TOF measurement for protons and heavy particles
Particle ID
Neutron detector array
Acceptance = 100 ~ 300 mSr
∆E/E ~ 5.0 x 10-2 via TOF measurements

## Slide 8
2. Neutron detectors for high-energy experiment
Proposed structure: 4 layers of plastic scintillators (2-m long)
+ 1 Veto plastic layer for charged particle rejection
Each layer composed of 40 10-cm-thick bar detector (20 of each for x and y directions)
Energy range: 30 ~ 300 MeV (10 MeV for the minimum detection)
Acceptance ~ 100 mSr when installed at 15 m from the target
∆E/E ~ 2 x 10-2 via TOF measurements
→ Required σ for 100 MeV neutrons ~ 500 ps
ε = 0.60 for single-neutron detection (100 MeV) (GEANT4)

## Slide 9
n-p elastic scattering
n-12C elastic scattering
n+p → d+γ (neutron capture, Eγ = 2.23 MeV)
n+12C → 13C+γ (neutron capture, Eγ = 1.2, 3.6, 4.9 MeV)
Single detector module for high-energy experiment

## Slide 10
Time-Of-Flight for γ and n
TOF distance = 1.0 m
Used LeCroy 2228 TDC & 2249 ADC
5-cm thick 5-cm diameter disk-shape plastic scintillator for event triggers
Maximum TOF to measure = 50 ns
3.78 n per fission decay and γ’s from gamma transitions
Trigger detector Neutron detector
γ γ
n γ
γ n
n n
1-m long neutron detector (2012-2013): Test results with 60Co & 252Cf sources
Event triggers

## Slide 11
From Left PMT
From Right PMT
TOF measurement for fission neutrons and gammas from 252 Cf
tL
tR

## Slide 12
Electronic setup
Maximum/Minimum times to measure (LeCroy 2228) for 252Cf neutrons: 20 ns/50 ns
Charge range measured by ADC (LeCroy 2249) = 100 fC ~ 25.6 pC
Digitization threshold for neutrons & gammas
Voltage-threshold discriminator (140 mV)
Constant-fraction discriminator (35 mV/ns, 4 ns sampling for trigger)
TOF of a neutron event = mean arrival time
(tL + tR)/ 2
→ t0 for time calibration by using the mean arrival time of gammas
→ Neutron energy
Position of the signal obtained from
∆t = tL - tR
→ Hit positions of neutrons along the bar detector

## Slide 13
Position resolution using a 60Co source
∆t = tL - tR

## Slide 14
Intrinsic time resolution measured using a 60Co source
Time-walk correction for signals
Accuracy of measuring (tL + tR)/ 2

## Slide 15
Testing a 1-m bar unit detector for high-energy experiments
Time resolution < 600 ps
Position resolution ~ 8.0 cm
Electron-equivalent energy with 50% efficiency ~ 700 keV
Neutron energy with 50% efficiency ~ 5 MeV
J. Kor. Phys. Soc. 58 (2011) 211
J. Kor. Phys. Soc. 62 (2013) 1227
Compton edge for 1.17 & 1.33 MeV γ’s from 60Co ~ 1.0 MeV
700 keV
ε ~ 50%
5 MeV

## Slide 16
Testing 2-m neutron detectors with 60Co & 252Cf sources (2014)
Manufactured 4 real-sized detector modules to check the feasibility for the proposed detector system
Detector R&D with 2 detector layers will be tested with TOF distance > 2.0 m
Neutron-hit structure
Multi-neutron events

## Slide 17
n
Υ
n
Υ
Electronic setup for preliminary tests
TOF distance = 1.0 m
Maximum/Minimum time to measure (LeCroy 2228) for 252Cf neutrons: 20 ns/50 ns
Charge range measured by ADC (LeCroy 2249) = 100 fC ~ 25.6 pC
Digitization threshold for neutrons & gammas
Voltage-threshold discriminator (180 mV)
Neutron energy with 50% efficiency ~ 4.5 MeV
The realistic time resolution should be measured with high-energy cosmic muons
Then, σ ~ 300 ps or less

## Slide 18
3. Neutron detectors for low-energy experiment
Neutron energy range to detect with ε > 0.7 = 2.5 ~ 30 MeV
Minimum detectable energy ~ 1 MeV with a maximum 200-ns TOF measurement
Basic structure of unit pixel detector: 3 x 3 detector modules
Single detectors: 10 x 10 x 20-cm3 plastic scintillator blocks
Neutron energies measured by a TOF method
∆E/E ~ 5.0 x 10-2 assuming a 3-m-long TOF length
Depth-of-interaction in the 20-cm long detector → Energy resolution

## Slide 19
Simulation for 18.5-AMeV 132Sn+124Sn collisions in low-energy LAMPS experiment (Y. J. Kim, IBS)
Angular Distributions for
γ, n, p, d, 3He, and 4He
PHITS (Particle and Heavy Ion Transport code System)
HI collision experiments for Symmetry-Energy with Ebeam < 20 AMeV

## Slide 20
Single detectors using conical-shape light guides (3, 5, 21-cm long)
Unit detector module composed of 4-plastic scintillator blocks

## Slide 21
Test with a 252Cf source
Specification of electronics
Utilized LeCroy-2228 TDC & LeCroy-2249 ADC
Digitization with a CFD
(30 mV/ns, 4 ns sampling for trigger)

## Slide 22
Pixel detectors for low-energy experiments
Maximum TOF set to 80 ns
→ 1.4 MeV neutrons (efficiency ~ 0.2)
Electron-equivalent energy with 50% efficiency ~ 300 keV
Neutron energy with 50% efficiency ~ 2.2 MeV
Advantage of using pixel detectors
Light-collection efficiency is higher
Expect reconstruction of neutron hits becomes easier
→ Much conducive to analyze low-energy multi-neutron events
ε ~ 50%
2.2 MeV

## Slide 23
4. TOF detectors in LAMPS Solenoid Spectrometer
Plastic-scintillator array surrounding the TPC for track-matching for charged particles & nuclear fragments
~ 40 (80) modules equipped one PMT on each side
2.0-m-long, 10-(5)cm wide, and 2-cm thick
Thinner plastic bars → less sensitive to scattered neutrons

## Slide 24
Digitization electronics
Unified module for digitization (CFD) + time measurement + charge measurement
(multi-hit TDC+FADC)
16-channel module with Lemo inputs
Single slot 9u VME type
Bandwidth = 500 MHz
Best time resolution ~ 100 ps
Sensitivity of each sampling: 50 fC minimum/ 200 pC
Minimum/Maximum sampling time interval = 2 ns/50 ns
Minimum/Maximum sampling time interval = 2.5 μs/64 μs
Data bus from the experimental area to the counting bay
Data rate ~ 3.5 GBps
200 detectors for neutron
100 detectors charged particle TOF
5. Digitization electronics for neutron & TOF detectors

## Slide 25: 6. Summary & milestones
  1. R&Ds of neutron detectors for LAMPS
  Conceptual designs of the neutron detectors
  Systematic R&Ds for unit detectors with 60Co & 252Cf source
  So far, confirmed that the proposed designs and the performances of the unit-detector are relevant and satisfactory for Symmetry-Energy researches
  2. Bar-shape neutron detectors for high-energy experiments
  Detectable range of neutron energy confirmed > 5.0 MeV
  Time resolution tested with low-energy radiation source ~ 600 ps
  Expected ~ 300 ps for high-energy particle (can be tested with cosmic muons)
  → ∆E/E ~ 2 x 10-2 via TOF measurements at 15 m from a target
  Position resolution confirmed ~ 8 cm

## Slide 26
  3. Pixel-type neutron detectors for low-energy experiments
  Minimum neutron energy confirmed with ε > 50% < 2.5 MeV
  Depth-of-interaction of 20-cm-long detectors: σ ~ 7.0 cm at a 3.0-m TOF distance
  → ∆E/E ~ 5 x 10-2 via TOF measurements
  4. Plans for LAMPS neutron detectors
  R&D for a 2-layer mini detector system for high-energy experiments
  R&D for a unit-detector composed of 7 scintillators low-energy experiments
  Study of neutron-hit structures (currently GEANT4 only)
  Discrimination for multi-neutron-hits (currently GEANT4 only)
  Discrimination of neutron from gamma backgrounds
  5. Designs of electronics and DAQ for LAMPS neutron detectors
  Combined 16-channel modules for discriminations, time (multi-hit TDC) and charge (FADC) measurements
  3.5 Gbps data bus electrons
  Data-acquisition system + GUI

## Slide 27: Backup

## Slide 28: RAON: Rare Isotope Accelerator Facility
SCL
IFF LINAC
Future extension
200 MeV/u, 9Ⅹ108pps(132Sn)
200 MeV/u, 8puA (U)
Stripper
28GHz SC ECR IS
Cyclotron
p: 70/100MeV, 1mA
SCL
RFQ
SCL
H2+
D+
17.5 MeV/u
ISOL LINAC
SCL
ECR IS
Fragment
Separator
Nuclear Astrophysics
Material Science
Medical/Bio Science
Medical Science
Low-energy experiments
Atomic
Physics
High-energy
experiments
ISOL
target
In-flight
target
β=0.041, β=0.085
QWR QWR
β=0.285, β=0.53
HWR HWR
β=0.10
QWR
β=0.04
QWR
Nuclear Data
400KW
70KW
Stripper
Nuclear Data
RFQ
Nuclear Physics
  RAON user community

## Slide 29: Importance of Symmetry Energy
A.W. Steiner, M. Prakash, J.M. Lattimer and P.J. Ellis, Physics Report 411, 325 (2005)
Effective field theory, QCD
isodiffusion
isotransport
+ isocorrelation
isofractionation
isoscaling
p-/p+
K+/K0
n/p
3H/3He
g

## Slide 30
Ion Species | Z/ A | Ion source output |  | SC linac output |  |  | 
 |  | Charge | Current (pµA) | Charge | Current (pµA) | Energy (MeV/u) | Power (kW)
Proton | 1/ 1 | 1 | 660 | 1 | 660 | 610 | 400
Ar | 18/ 40 | 8 | 42.1 | 18 | 33.7 | 300 | 400
Kr | 36/ 86 | 14 | 22.1 | 34-36 | 17.5 | 265 | 400
Xe | 54/ 136 | 18 | 18.6 | 47-51 | 12.5 | 235 | 400
U | 92/ 238 | 33-34 | 11.7 | 77-81 | 8.4 | 200 | 400
IFF Linac Beam Specification
Isotope | Half-life | Yield at target (pps) | Overall eff. (%) | Expected Intensity (pps)
78Zn | 1.5 s | 2.75 x 1010 | 0.0384 | 1.1 x 107
94Kr | 0.2 s | 7.44 x 1011 | 0.512 | 3.8 x 109
97Rb | 170 ms | 7.00 x 1011 | 0.88 | 6.2 x 109
124Cd | 1.24 s | 1.40 x 1012 | 0.02 | 2.8 x 108
132Sn | 40 s | 4.68 x 1011 | 0.192 | 9.0 x 108
133In | 180 ms | 1.15 x 1010 | 0.184 | 2.1 x 107
142Xe | 1.22 s | 5.11 x 1011 | 2.08 | 1.1 x 1010
Estimated RIBs based on ISOL
30
  RAON user community

## Slide 31
RIB species | ISOL (pps) | In-Flight Fragmentation (pps) | Comment
15O | 5x108 via 19F(p,αn), LiF pressed powder | To be estimated | Nuclear astropysics
94Kr | 4x109 | 4x102 | Nuclear structure
109Y | 2x105 | <102 | New discovery at RIKEN
117Mo | Not available due to low vapor pressure | <103 | New discovery at RIKEN
132Sn | 9x108 | 2x105 | Symmetry energy for double magic
142Xe | 1x1010 | 1x104 | Symmetry energy
144Cs | 7x108 | 3x104 | Nuclear astrophysics
RAON RI Beam intensities compared for ISOL & IFF
  KoRIA user community
31
  RAON user community

## Slide 32: Experimental Observables
Signals at sub-saturation densities
  Sizes of n-skins for unstable nuclei
  n/p ratio of fast, pre-equilibrium nucleons
  Isospin fractionation and isoscaling in nuclear multifragmentation
  Isospin diffusion (transport)
  Differential collective flows (v1 & v2) of n and p
  Correlation function of n and p
  3H/3He ratio, etc.
Signals at supra-saturation densities
  π-/π+ ratio
  Differential collective flows (v1 & v2) of n and p
  Azimuthal angle dependence of n/p ratio with respect to the R.P.
Correlation of various observables
Simultaneous measurement of neutrons and charged particles

## Slide 33
Assuming Perfect Time Resolution
Assuming st = 1 ns
Edet estimated by ToF

## Slide 34
Assuming Perfect Time Resolution
Assuming finite st

## Slide 35
LINAC
Experimental Hall
Beam line [for acceleration]
Beam line [for experiment]
Target building
IFF LINAC
ISOL LINAC
Future plan
Stripper
SC ECR IS
Cyclotron
K~100
Fragment
Separator
Charge
Breeder
SCL
RFQ
RFQ
SCL
SCL
Low energy experiments
70 kW ISOL
target
400 kW
In-flight
target
μ, Medical
research
Atom trap
experiment
H2+
D+
Nuclear Astrophysics
Material science
Bio science
Nuclear data
Atomic / Nuclear physics
Medical science
Nuclear Physics
Future extension area
ISOL with cyclotron driver (70 kW)
High energy
experiments
  RAON user community
200 MeV/u, 9Ⅹ108pps(132Sn)
200 MeV/u, 8puA (U)
28GHz SC ECR IS
Stripper
18.5 MeV/u

## Slide 36
Layer Number vs. ToF
Efficiency as a function of
the distance from the target

## Slide 37: 1. Introduction
ISOL+IFF+ISOL
Nuclear data using fast neutrons
Basic data for future nuclear energy
Radioactive waste transmutation
Nuclear Astrophysics
Origin of nuclei
Paths of nucleosynthesis
Neutron stars and supernovae
Material science
Production & Characterization of new materials
Dynamic image in nm scale
Nuclear Physics
Exotic nuclei near the neutron drip line
Super-Heavy Elements (SHE)
Equation-of-state (EoS) of nuclear matter
Atomic physics
Limits of nuclear existence
Fundamental conservation law
Medical and Bio sciences
Advanced therapy technology
Mutation of DNA
ISOL+IFF+ISOL(Trap)
RAON: Rare Isotope Accelerator Facility
  RAON user community

## Slide 38
200 MeV/u, 9Ⅹ108pps(132Sn)
200 MeV/u, 8puA (U)
18.5 MeV/u
RAON: Rare Isotope Accelerator Facility
28GHz SC ECR IS

## Slide 39
High intensity RI beams by ISOL & IFF
  70 kW ISOL from direct fission of 238U induced by 70 MeV and 1 mA proton cyclotrons
  400 kW IFF by 200 MeV/u, 8 pμA 238U
High energy, high intensity neutron-rich RI beams
  132Sn, 142Xe at ~250 MeV/u with intensity > 108 pps
Exploring more exotic RI beams by using multi-step RI production processes by combining ISOL & IFF
Design for maximal use of the facility for basic nuclear physics and applications
RAON: Specification
  RAON user community

## Slide 41
Bao-An Li, PRL 88, 192701 (2002)
Phys Rep. 464 113 (2008)
High (Low) density matter is more neutron rich with soft (stiff) symmetry energy
LAMPS probes symmetry-energy up to ρ0/ρ ~ 2 with 200 AMeV
At nuclear matter density ρ > ρ0 ( = 0.16 fm-3)
Case 1: Easym(ρ) = Esym(ρ0) u, uc= ρ/ρ0
Case 2: Ebsym(ρ) = Esym(ρ0) u (uc – u)/(uc – 1), uc=ρ/ρ0
Case 1
Case 2
Case 1
Case 2

## Slide 42
FAIR
GSI
FRIB
LAMPS/RAON
RIBF
MSU
LAMPS/RAON: exploring a wide range of N/Z asymmetry
The symmetry energy at sub-saturation density and supra-saturation density with ~ 250 AMeV

## Slide 43
  Si-CsI arrays
  Energy measurement and particle ID for both nuclear fragments and γ’s
  100 μm thick Si
  50-mm thick CsI
  Full absorption for all charged particles
  ε > 70% for γ’s
  Another solution
  Thin plastic-CsI arrays for measurement of lower-energy HI fragments
  Particle occupancies (PHITS)
  Black: all charge particles
  Red: γ BLUE: protons