## Slide 1: LAMPS Time Projection Chamber
HyoSang Lee
IBS
2014.03.31

## Slide 2
300 mm
900 mm
500 mm
400 mm
53.1°
24.0°
h=-0.7 (127o)
h=1.6 (24o)
Beam
150 mm
Target
LAMPS High Energy
Complete information of charged particle trajectory
Detection range : -0.7(127o) ~ 1.6(24o)
Volume : 857L
Cathode Membrane
Both side readout PAD
Target : 30cm away from the center
Inside of Solenoid magnet
LAMPS TPC
Design Concept of p.TPC for LAMPS

## Slide 3
Time Projection Chamber
Design Concept of p.TPC for LAMPS
Concept of prototype TPC for LAMPS
Optimized design & fabrication method : 1/2 size of real TPC (1/8 volume) Honeycomb body for gas chamber
PAD : Hexagon shape
  Test with 5mm & 2.5mm
GEM : Test with large size & specific shape
Field cage : Uniform electric field by cu strip
DAQ : COBO system
Analysis : Development of reconstruction algorism

## Slide 4
Prototype TPC
Prototype TPC for LAMPS
Bottom to fix PAD & GEM : Al
Inner Field Cage
Outer Field Cage
Cathode
GEM : 3 layers
PAD
150 mm
640 mm
490 mm
½ size of real TPC design

## Slide 5
PAD
Prototype TPC for LAMPS
Hexagonal shape : 5mm & 2.5mm
500 mm gap between two pads
Multi-layer PCB board
Trapezoidal (or Octant) shape PCB
4 layers PCB
16 pin SMD type connector (1.27mm pitch)
5 mm pad
(207 ch)
2.5 mm pad (735 ch)
Trapezoidal (or Octant) shape PCB
MAYA pattern

## Slide 6
PAD
Prototype TPC for LAMPS
5mm PAD : 207ch
2.5mm PAD : 735ch
16pin SMD connector
PAD PCB design
PAD installed in bottom frame

## Slide 7
GEM
Design Concept of p.TPC for LAMPS
Trapezoidal shape
50mm & 75mm thickness
160x120 mm2
3 layers for each PAD

## Slide 8
GEM
Prototype TPC for LAMPS
Electrode
Divided
20cm
10cm
Electrode
3 layers
Dummy cathode
69mm
118mm
166mm

## Slide 9
Field Cage
Prototype TPC for LAMPS
35 um thick and 2 mm wide Cu strips
0.5 mm gap between neighboring strips
Mirror strips on the back
1 MW resistors with 0.1% var.
TPC body: G10 + Aramid honeycomb
Cross-section of field-cage body
G10
HoneyComb
Al Mylar
GRP
GRP
Mirror strip
PI
Field strip
1MOhm resistor(0.1%)

## Slide 10
Field strip
Mirror strip
2mm
0.5mm
PI : 75um
Cu : 35um
Field Cage
Prototype TPC for LAMPS
Field strip : resistor pattern
HV divider circuit for triple GEM

## Slide 11
Field Cage
Prototype TPC for LAMPS
E field sum : EFSUM=180V/cm
Potential distribution
570mm
Two resistors chain : ~228MW

## Slide 12
Field Cage
Prototype TPC for LAMPS
Field strip : outer (with 6 sheets)
Field strip : inner (with 2 sheets)
Field strip sheet with resistor pattern
Two resistor chain
Two resistor chain
Field strip sheet without resistor pattern
resistor pattern
electrode

## Slide 13
Field Cage
Prototype TPC
Target Holder
PAD + GEM
prototype TPC
fieldstrip
Fieldstrip + Gas chamber

## Slide 14
Field Cage test
Laser test
Laser direction
Laser source
p.TPC
p.TPC test @ J-PARC Hadron Hall
150V/cm
160V/cm
170V/cm
180V/cm
p.TPC – drift velocity

## Slide 15
Cathode
Prototype TPC for LAMPS
460mm
180mm
Dummy cathode
Cathode holder
HV connector hole

## Slide 16
Time Projection Chamber
Prototype TPC for LAMPS
TPC bottom frame : Al
TPC bottom with PAD
PAD frame (G10) & HV connector
TPC bottom
with PAD + GEM + dummy cathode
TPC bottom back
PAD connector
HV connector
HV connector

## Slide 17
Time Projection Chamber
Prototype TPC for LAMPS
G10 frame for Field Cage
720mm
490mm
Field Cage with G10 sheet
Field Cage with honeycomb
Field Cage with field strip
Inner Field Cage

## Slide 18
Time Projection Chamber
Prototype TPC for LAMPS
Inner Field Cage install
Outer Field Cage install
Prototype TPC
Prototype TPC : back

## Slide 19
Time Projection Chamber
Prototype TPC for LAMPS
GET system
TPC
ZAP
AsAd
CoBo
PC
ZAP board : to protect AGET chip in AsAd board
ASAD : AGET Support for Analog to Digital
A(Asic)GET chip
4 AGET (256 ch)
  in 1 AsAd
12 bit ADC
Pulsar
COBO : Collection BOard
Digital data from AsAd
Zero suppression
Network transfer to PC
4 AsAd controlled by 1 COBO
2nd version ZAP
BAV99 chip : small signal diode

## Slide 20
1 ASAD : 4GET  256ch
1 COBO : 4ASAD 1024ch
1 uTCA : 10COBO  10240ch
5mm size PAD : ~11000ch x 2  2~3 uTCA
2.5mm size PAD : ~44000ch x 2  8~9 uTCA
Time Projection Chamber
Prototype TPC for LAMPS

## Slide 21
Time Projection Chamber
Prototype TPC for LAMPS
Reduced-CoBo system – Virtual COBO with ML507

## Slide 24
GEM test with small chamber
Current Status
HV divider
GEM
ZAP board
PAD
Test
Readout PAD system
Characteristic of GEM
Gain of GEM
New GEM
Comparison of GEM of two domestic vendor

## Slide 25
Summary

## Slide 27
backup

## Slide 35
LAMPS prototype-TPC : Plan
Test plan
  Cosmic ray test : reconstruct muon track
  Fe-55 source test
  ExB test in the magnet