## Slide 1: LAMPS Time Projection Chamber
HyoSang Lee
High Energy Nuclear Science Team
Rare Isotope Science Project
Institute for Basic Science
LAMPS Review
2014.03.31

## Slide 2
LAMPS High Energy - heavy ion collisions - to study the symmetry energy in the EoS of nuclear matter - designed to cover wide acceptance range with high detection efficiency and accuracy of charged particles and neutrons
Time Projection Chamber (TPC) - main detector for tracking of particles - complete information of charged particle trajectory - inside of Solenoid magnet
LAMPS TPC

## Slide 3
300 mm
900 mm
500 mm
400 mm
53.1°
24.0°
h=-0.7 (127o)
h=1.6 (24o)
Beam
150 mm
Target
LAMPS TPC
Target : 30cm away from the center
Detection range : -0.7(127o) ~ 1.6(24o)
Drift length : 60cm (x2)
Volume : 857L
Cathode Membrane
Amplified by Gas Electron Multiplier (GEM)
Both side readout PAD

## Slide 4
1st prototype TPC
Prototype TPC
PAD + GEM
fieldstrip
Purpose of 1st prototype TPC
Uniform electric field  by Cu strip
3 layers GEM
TPC body : G10 material

## Slide 5
1st prototype TPC
Prototype TPC
Electrode
Divided
20cm
10cm
150V/cm
160V/cm
170V/cm
180V/cm
Field strip
GEM
10cm x 20cm
3 layers
Divided by two section
1 MW resistors with 0.1% var.

## Slide 6
Design
Concept of prototype TPC for LAMPS
Optimized design & fabrication method : 1/2 size of real TPC (1/8 volume) Honeycomb body for gas chamber
PAD : Hexagon shape
  Test with 5mm & 2.5mm
GEM : Test with large size & specific shape
Field cage : Uniform electric field by cu strip
DAQ : COBO system
Analysis : Development of reconstruction algorism
Prototype TPC for LAMPS

## Slide 7
Design
Prototype TPC for LAMPS
Bottom to fix PAD & GEM : Al
Inner Field Cage
Outer Field Cage
Cathode
GEM : 3 layers
PAD
150 mm
Drift length : 570 mm
490 mm
½ size of real TPC design

## Slide 8
PAD
Prototype TPC for LAMPS
Hexagonal shape : 5mm & 2.5mm
500 mm gap between two pads
Multi-layer PCB board
Trapezoidal (or Octant) shape PCB
4 layers PCB
16 pin SMD type connector (1.27mm pitch)
5 mm pad
(207 ch)
2.5 mm pad (735 ch)
Trapezoidal (or Octant) shape PCB
MAYA pattern

## Slide 9
PAD
Prototype TPC for LAMPS
5mm PAD : 207ch
2.5mm PAD : 735ch
16pin SMD connector
PAD PCB design
PAD installed in bottom frame

## Slide 10
GEM
Design Concept of p.TPC for LAMPS
Trapezoidal shape
50mm & 75mm thickness
160x120 mm2
3 layers for each PAD

## Slide 11
Electrode
Divided
20cm
10cm
Electrode
3 layers
Dummy cathode
69mm
118mm
166mm
GEM
Design Concept of p.TPC for LAMPS

## Slide 12
Field Cage
Prototype TPC for LAMPS
35 um thick and 2 mm wide Cu strips
0.5 mm gap between neighboring strips
Mirror strips on the back
1 MW resistors with 0.1% var.
TPC body: G10 + Aramid honeycomb
Cross-section of field-cage body
G10
HoneyComb
Al Mylar
GRP
GRP
Mirror strip
PI
Field strip
1MOhm resistor(0.1%)

## Slide 13
Field strip
Mirror strip
2mm
0.5mm
PI : 75um
Cu : 35um
Field Cage
Prototype TPC for LAMPS
Field strip : resistor pattern
HV divider circuit for triple GEM

## Slide 14
Field Cage
Prototype TPC for LAMPS
E field sum : EFSUM=180V/cm
Potential distribution
570mm
Two resistors chain : ~228MW

## Slide 15
Field Cage
Prototype TPC for LAMPS
Field strip : outer (with 6 sheets)
Field strip : inner (with 2 sheets)
Field strip sheet with resistor pattern
Two resistor chain
Two resistor chain
Field strip sheet without resistor pattern
resistor pattern
electrode

## Slide 16
Cathode
Prototype TPC for LAMPS
460mm
180mm
Dummy cathode
Cathode holder
HV connector hole
Cathode
Cathode holder

## Slide 17
Assembling
Prototype TPC for LAMPS
TPC bottom frame : Al
TPC bottom with PAD
PAD frame (G10) & HV connector
TPC bottom
with PAD + GEM + dummy cathode
TPC bottom back
PAD connector
HV connector
HV connector

## Slide 18
G10 frame for Field Cage
720mm
490mm
Field Cage with G10 sheet
Field Cage with honeycomb
Field Cage with field strip
Inner Field Cage
Assembling
Prototype TPC for LAMPS

## Slide 19
Inner Field Cage install
Outer Field Cage install
Prototype TPC
Prototype TPC : back
Assembling
Prototype TPC for LAMPS

## Slide 20
GET system
DAQ
GET system
TPC
ZAP
AsAd
CoBo
PC
ZAP board : to protect AGET chip in AsAd board
ASAD : AGET Support for Analog to Digital
A(Asic)GET chip
4 AGET (256 ch)
  in 1 AsAd
12 bit ADC
Pulsar
COBO : Collection BOard
Digital data from AsAd
Zero suppression
Network transfer to PC
4 AsAd controlled by 1 COBO
2nd version ZAP
BAV99 chip : small signal diode

## Slide 21
R-CoBo system
DAQ
Reduced-CoBo system – Virtual COBO with ML507

## Slide 22
1 ASAD : 4GET  256ch
1 COBO : 4ASAD 1024ch
1 uTCA : 10COBO  10240ch
5mm size PAD : ~11000ch x 2  2~3 uTCA
2.5mm size PAD : ~44000ch x 2  8~9 uTCA
GET system
DAQ

## Slide 23
NARVAL
TPC
GET system
NARVAL (Nouvelle Acquisition temps Réel Version 1.6 Avec Linux)
  runs across a network and acts like a unique program taking data out of the electronic up to providing data to physicist (storage, histogram display and etc). - highly distributed acquisition system - developed in Ada (but actors can load C/C++ shared library)
  a lots of system to support
  runs many acquisitions in parallel
DAQ

## Slide 24
GEM test with small chamber
Current Status
HV divider
GEM
ZAP board
PAD
Test
Readout PAD system
Characteristic of GEM
Gain of GEM
New GEM
Comparison of GEM of two domestic vendor

## Slide 25
Summary
LAMPS High Energy - heavy ion collisions experiment to study the symmetry energy in the EoS of nuclear matter - designed to cover wide acceptance range with high detection efficiency and accuracy of charged particles and neutrons
Time Projection Chamber (TPC) - main detector for tracking of particles - complete information of charged particle trajectory - Target : 30cm away from the center - Detection range : -0.7(127o) ~ 1.6(24o) - Drift length : 60cm (x2) - Cathode Membrane - Amplified by Gas Electron Multiplier (GEM) - Both side readout PAD
Concept of prototype TPC for LAMPS - Optimized design & fabrication method : 1/2 size of real TPC (1/8 volume), Honeycomb body for gas chamber - PAD : Hexagon shape with 5mm & 2.5mm - GEM : Test with large size & specific shape - Field cage : Uniform electric field by Cu strip - DAQ : COBO system - Analysis : Development of reconstruction algorism
Current status - GEM & PAD test with source

## Slide 28
Thank you for your attention

## Slide 29
backup