## Slide 1
J. Ahn4, B. Hong1, E. Joo1, E. Kim3, H. Kim3, Y. J. Kim2, Y. K. Kim2, Y. J. Ko1, K. S. Lee1, J. W. Lee1, H. Lee4, K. S. Lee1, S. Lee1, B. Mulilo1, T. S. Shin2
1Korea University, Seoul, Korea
2Institute for Basic Science, Daejeon, Korea 3Chonbuk National University, Jeonju, Korea
4Pusan National University, Busan, Korea
Plastic Scintillators for Neutron and Charge Particle Detections for LAMPS Experiments at RAON
Contents
Introductions: LAMPS at RAON
Neutron detectors for high-energy experiments
Neutron detectors for low-energy experiments
TOF detectors in LAMPS solenoid spectrometer
Digitization electronics for neutron and TOF detectors
Summary & milestones

## Slide 2: 1. Introductions: LAMPS at RAON
Large Acceptance Multi-Purpose Spectrometer to maximize the use of nuclear physics researches for neutron-rich nuclei
  Main purpose for Symmetry-Energy research
  Understanding astronomical phenomena in neutron stars, black holes, and super novae by the EOS of nuclear matter at high density
  Pygmy Dipole & Giant Dipole Resonances
  Neutron halos and exotic nuclei lying near neutron drip lines
  2. Conceptual designs of LAMPS
  High-energy experiment (250 AMeV)
  Solenoid spectrometer equipped with a 3π-Sr TPC
  Dipole spectrometer with a focal plane detector system
  Large acceptance of neutron detectors via TOF measurement
  Low-energy experiment (< 20 AMeV)
  Vacuum system equipped with Si-CsI detectors
  Large acceptance of neutron detectors via TOF measurement

## Slide 3
LAMPS: design for high-energy experiment
Solenoid spectrometer
Solenoid magnet (0.6 ~ 1.5 T)
TPC (∆P/P ~ 10-2)
Si-CsI array (∆E/E ~ 10-2)
Plastic barrel detectors for trigger
Dipole spectrometer
Quadruple-Dipole magnets
(QD or QQD) for focal plane (∆P/P ~ 4 x 10-4)
Drift chambers
TOF wall
Neutron detector array
Acceptance ~ 34 mSr
∆E/E < 2 x 10-2

## Slide 4
LAMPS: design for low-energy experiment
Vacuum chamber
Si-CsI array (charged particles & γ)
∆E/E ~ 10-2
TOF measurement for protons and heavy particles
Particle ID
Neutron detector array
Acceptance = 100 ~ 300 mSr
∆E/E ~ 5.0 x 10-2 via TOF measurements

## Slide 5
2. Neutron detectors for high-energy experiment
Proposed structure: 4 layers of plastic scintillators (2-m long)
+ 1 Veto plastic layer for charged particle rejection
Each layer composed of 40 10-cm-thick bar detector (20 of each for x and y directions)
Energy range: 30 (10) ~ 300 MeV (10 MeV for the minimum detection)
Acceptance ~ 34 mSr when installed at 10 m from the target
∆tTOF/tTOF ~ 5 x 10-3 for 100 MeV at 10-m TOF
∆E/E < 2 x 10-2 via TOF measurements
→ Required σt for 100 MeV neutrons ~ 500 ps
ε = 0.60 for single-neutron detection (100 MeV) (GEANT4)

## Slide 6
n-p elastic scattering
n-12C elastic scattering
n+p → d+γ (neutron capture, Eγ = 2.23 MeV)
n+12C → 13C+γ (neutron capture, Eγ = 1.2, 3.6, 4.9 MeV)
Single detector module for high-energy experiment

## Slide 7
Time-Of-Flight for γ and n
TOF distance = 1.0 m
Used LeCroy 2228 TDC & 2249 ADC
5-cm thick 5-cm diameter disk-shape plastic scintillator for event triggers
Maximum TOF to measure = 50 ns
3.78 n per fission decay and γ’s from gamma transitions
Trigger detector Neutron detector
γ γ
n γ
γ n
n n
1-m long neutron detector (2012-2013): Test results with 60Co & 252Cf sources
Event triggers

## Slide 8
From Left PMT
From Right PMT
TOF measurement for fission neutrons and gammas from 252 Cf
tL
tR

## Slide 9
Electronic setup
Maximum/Minimum times to measure (LeCroy 2228) for 252Cf neutrons: 20 ns/50 ns
Charge range measured by ADC (LeCroy 2249) = 100 fC ~ 25.6 pC
Digitization threshold for neutrons & gammas
Voltage-threshold discriminator (140 mV)
Constant-fraction discriminator (35 mV/ns, 4 ns sampling for trigger)
TOF of a neutron event = mean arrival time
(tL + tR)/ 2
→ t0 for time calibration by using the mean arrival time of gammas
→ Neutron energy
Position of the signal obtained from
∆t = tL - tR
→ Hit positions of neutrons along the bar detector

## Slide 10
Position resolution using a 60Co source
∆t = tL - tR

## Slide 11
Intrinsic time resolution measured using a 60Co source
Time-walk correction for signals
Accuracy of measuring (tL + tR)/ 2

## Slide 12
Testing a 1-m bar unit detector for high-energy experiments
Time resolution < 600 ps
Position resolution ~ 8.0 cm
Electron-equivalent energy with 50% efficiency ~ 700 keV
Neutron energy with 50% efficiency ~ 5 MeV
J. Kor. Phys. Soc. 58 (2011) 211
J. Kor. Phys. Soc. 62 (2013) 1227
Compton edge for 1.17 & 1.33 MeV γ’s from 60Co ~ 1.0 MeV
700 keV
ε ~ 50%
5 MeV

## Slide 13
Testing 2-m neutron detectors with cosmic muons, 60Co, and 252Cf sources (2014)
Manufactured 4 real-sized detector modules to check the feasibility for the proposed detector system
Detector R&D with 2 detector layers will be tested with TOF distance of 2.0 m
Neutron-hit structure
Multi-neutron events

## Slide 14
n
γ
Electronic setup for preliminary tests
TOF distance = 1.0 m
Maximum/Minimum time to measure (LeCroy 2228) for 252Cf neutrons: 20 ns/50 ns
Charge range measured by ADC (LeCroy 2249) = 100 fC ~ 25.6 pC
Digitization threshold for neutrons & gammas
Voltage-threshold discriminator (180 mV)
Neutron energy with 50% efficiency ~ 4.5 MeV
The realistic time resolution should be measured with high-energy cosmic muons
Then, σ ~ 300 ps
n
γ

## Slide 15
3. Neutron detectors for low-energy experiment
Neutron energy range to detect with ε > 0.7 = 2.5 ~ 30 MeV
Minimum detectable energy ~ 1 MeV with a maximum 200-ns TOF measurement
Basic structure of unit pixel detector: 3 x 3 detector modules
Single detectors: 10 x 10 x 20-cm3 plastic scintillator blocks
Neutron energies measured by a TOF method
∆E/E ~ 5.0 x 10-2 assuming a 3-m-long TOF length
Depth-of-interaction in the 20-cm long detector → Energy resolution

## Slide 16
16
HI collisions for 132Sn+124Sn
Ebeam = 18.5 AMeV

## Slide 17
HI collisions for 132Sn+124Sn (Ebeam = 18.5 AMeV)
θ distribution for neutrons
θ distribution for charged particles

## Slide 18
Occupancy for neutrons
Kinetic energies for neutrons

## Slide 19
Single detectors using conical-shape light guides (3, 5, 21-cm long)
Unit detector module composed of 4-plastic scintillator blocks

## Slide 20
Test with a 252Cf source
Specification of electronics
Utilized LeCroy-2228 TDC & LeCroy-2249 ADC
Digitization with a CFD
(30 mV/ns, 4 ns sampling for trigger)

## Slide 21
Pixel detectors for low-energy experiments
Maximum TOF set to 80 ns
→ 1.4 MeV neutrons (efficiency ~ 0.2)
Electron-equivalent energy with 50% efficiency ~ 300 keV
Neutron energy with 50% efficiency ~ 2.5 MeV
Advantage of using pixel detectors
Light-collection efficiency is higher
Expect reconstruction of neutron hits becomes easier
→ Much conducive to analyze low-energy multi-neutron events
ε ~ 50%
2.5 MeV

## Slide 22
4. TOF detectors in LAMPS Solenoid Spectrometer
Plastic-scintillator array surrounding the TPC for track-matching for charged particles
40 modules equipped one PMT on each side
1.5-m-long, 10-cm wide, and 2.5-cm thick
Chosen thin plastic bars → less sensitive to scattered neutrons

## Slide 23
Digitization electronics
Unified module for digitization (CFD) + time measurement + charge measurement
(multi-hit TDC+FADC)
16-channel module with Lemo inputs
Single slot 9u VME type
Bandwidth = 500 MHz
Best time resolution ~ 100 ps
Sensitivity of each sampling: 50 fC minimum/ 200 pC
Minimum/Maximum sampling time interval = 2 ns/50 ns
Minimum/Maximum sampling time interval = 2.5 μs/64 μs
Data bus from the experimental area to the counting bay
Data rate ~ 3.5 GBps
200 detectors for neutron detector
40 detectors charged particle TOF
5. Digitization electronics for neutron & TOF detectors

## Slide 24: 6. Summary & milestones
  1. R&Ds of neutron detectors for LAMPS
  Conceptual designs of the neutron detectors
  Systematic R&Ds for unit detectors with 60Co & 252Cf source
  So far, confirmed that the proposed designs and the performances of the unit-detector are relevant and satisfactory for Symmetry-Energy researches
  2. Bar-shape neutron detectors for high-energy experiments
  Minimum neutron energy confirmed with ε > 50% was 5.0 MeV
  Time resolution tested with low-energy radiation source < 600 ps
  But, expected ~ 300 ps for high-energy particle (can be tested with cosmic muons)
  → ∆E/E < 2 × 10-2 via TOF measurements at 10 m from a target
  Position resolution confirmed ~ 8 cm

## Slide 25
  3. Pixel-type neutron detectors for low-energy experiments
  Minimum neutron energy confirmed with ε > 50% was 2.5 MeV
  Depth-of-interaction of 20-cm-long detectors: σ ~ 7.0 cm at a 3.0-m TOF distance
  → ∆E/E ~ 5 × 10-2 via TOF measurements
  4. Plans for LAMPS neutron detectors
  R&D for a 2-layer mini detector system for high-energy experiments
  R&D for a unit-detector composed of 7 scintillators low-energy experiments
  Study of neutron-hit structures (currently GEANT4 only)
  Discrimination for multi-neutron-hits (currently GEANT4 only)
  Discrimination of neutron from gamma backgrounds
  5. Designs of electronics and DAQ for LAMPS neutron detectors
  Combined 16-channel modules for discriminations, time (multi-hit TDC) and charge (FADC) measurements
  3.5 Gbps data bus electrons
  Data-acquisition system + GUI