## Slide 1
D-RD-19
LiquidO R&D: Novel Detector Concept
for Neutrino Experiments
A. Cabrera: CNRS/IN2P3, LAL, LNCA, France
F. Suekane: Tohoku Univ. Japan
Joint workshop of FKPPL & TYL/FJPPL :
@ Jeju Island, Korea 2019/05/10

## Slide 2
Contents
* D-RD-9 group
* About LiquidO Detector
* 2018 achievement
* 2019 plan

## Slide 3
LAL/IN2P3: C. Anatael, M.Grassi
SUBATECH: Y.Frederic, V.Benoit, J. Thiago
CENBG: M.Christine, C.Emmanuel
CPPM: B.Jose
Tohoku U.: F.Suekane
FJPPL Project Members

## Slide 4
Publication:
* Neutrino-Antineutrino Identification in a Liquid Scintillator Detector: Towards a Novel
Decay-at-Rest-based Neutrino CPV Framework.
Grassi M. et al. (LiquidO Team), arXiv:1807.04731
Talks:
* LiquidO Novel Detection Technique and ββ Program.
A.Cabrera, Conference: NOW-2018 Conference, Italy
* LiquidO Talk:
A.Cabrera, France ββ Physics Workshop (APC, Paris, France)
* LiquidO Talk:
A.Cabrera, https://indico.in2p3.fr/event/17804/contributions/64467/attachments/
49788/63356/2018Sept-LiquidO-France_Anatael.pdf

## Slide 5
* LiquidO is a detector technology to observe spatial pattern of signals
by using opaque LS and WLS fibers.
What is LiquidO?
Wave Length Shifting fibers
readout position, timing,
amplitude
Opaque (milky, cloudy, waxy)
LS
Scintillation lights are
confined in a small region

## Slide 6: Opaque scintillator→ new technology!
6

## Slide 7: For “O(1cm) resolution”…
dE/dx→ Bragg peak
(e- starts as MIP)
e- ≈ α ≈ p-recoil (fast-n)
e+ ≈ e- + 2x γ(511keV)
γ (gamma ray)
@ few MeV→ Compton scattering
(ended by photon-electric effect)
hybrid-like event
α and p are scintillation quenched→ PSD is possible!

## Slide 8
Common issue of low energy neutrino experiments
* Because neutrino interacts only Weakly, the event rate is generally very very small:
While backgrounds (gamma ray, cosmic ray related) are large.
* Tough issue of Neutrino Experiments = Battle against backgrounds.
* The low energy neutrino signals are often e-, e+, while the backgrounds come from
g and p recoiled by fast neutron.
* If separation of e-, e+  g  p can be done, the backgrounds can be removed.
* In addition, if e-  e+ can be separated, the original ne or can be separated.
* LiquidO technology is to measure the spatial pattern of those signals and separate them.

## Slide 9: Simplest LiquidO design: 2D⊕time…
(x,y) info → image pixelation
(z) info → time difference
(also z-pixelation possible→ envisaged for R&D)

## Slide 10
e+ 2MeV
e- 2MeV
γ 2MeV
If signal(e-) ⇒ rejection e+,γ
PID e-:γ ≈100:1 PRELIMINARY
Eventa pattern Simulation

## Slide 11
Physics possibilities …
    •improved geo-neutrino, including first 40K detection?
    •background-less reactor neutrino detection?
    •CP-Violation via νe & anti-νe
    •solar neutrino (including pp)?
    •supernova’s CC (νe & anti-νe) & NC?
    •multi-ton ββ & first observation β+β+?
    •unprecedented proton-decay capabilities?
    •TeV collider calorimetry?
    •technology: medical, non-proliferation
    :

## Slide 12
An example
Separation  CPV measurement
Clean CPV measurement using decay at rest neutrinos (arXiv:1807.04731)
* # of = # of 
* Negligible matter effect (L~15km)
* Energy spectra are perfectly known. 
: & other good things 
:
* >100ktons of target mass is necessary. 
But ... 40 years ago, no one expected there would be 1kton LS detector and 50kton
water cherenkov detector 20 years after.

## Slide 13
LiquidO R&D

## Slide 14
2 prototypes
m-LiquidO:
3 fibers
Mini-LiquidO:
many fibers

## Slide 15
e- position ≤1mm
e- energy ≤1%
Use monochromatic e- as scintillation source

## Slide 16
Change the opaque-ness
by changing temperature
and see the change of light yields of
F0, F1, F2 and the top PMT.
Scintillation light confinement will show ...
Transparency of LS
(Temperature)
F0
F1
F2
PM
Light Yield
Opaque

## Slide 17
x1/4
X2.5
x1/2
~transparent
~opaque
Measurement
LAB LS
Opaque-LS

## Slide 18
:4 :2
X1.1 X1.1

## Slide 19
:4 :2
:4 :1.5

## Slide 20
Opaque LS
all measurements
all lines are linear fits of data
Fiber 0 (bottom) Fiber 1 (middle) Fiber 2 (top) s
 Scintillation light
confinement

## Slide 21
LAB
Opaque LS
< F2
< F1
< F0
< F2
< F1
< F0
stacked Npe values
Total Light yield increased

## Slide 22
Micro-Liquid:
3 fibers
Mini-Liquid:
many fibers
2019~

## Slide 23
Mini-LiquidO Test detector

## Slide 24: Ω readout (single-layer)
detector vessel
readout
electronics
LED pulser

## Slide 25
WLS Fiber pattern
inside the Mini LiquidO
closed detector now (PMT window)

## Slide 26
Fiber route outside

## Slide 27: new readout

## Slide 28
Will see 1 MeV electron
signal pattern!!
 Data take in 2019.

## Slide 29
Summary
* LiquidO is a detector technology to observe the signal spatial pattern by using
opaque LS and WLS fibers.
* From the signal pattern, particle ID is possible and the backgrounds can be removed.
Charged current interaction of ne or can be separated.
* In 2018, the proof of principle of the scintillation light confinement was successfully
performed by using the m-LiquidO
* In 2019, we will measure the e- signal pattern by using Mini-LiquidO.
* R&D is continuing steadily....

## Slide 30
Back ups

## Slide 33: geo-ν(40K) detection ever?
33
Earth Formation Heat Contribution
hope to detect geo-ν(40K)? [impossible so far]
Cd-ν interaction: 40K and more! U⊕Th geo-ν’s?
40K-ν mystery
(volatility vs Earth center)

## Slide 34: from Double Chooz to LiquidO…
34
Signal:BG ≈ 10:1
Signal:BG ≈ ≥1000:1
[conservative]
cosmogenic rejection→ PID(e+:e-) ≥100x (expected ~1000x)
accidentals rejection→ ≥100x [time⊕space coincidence & PID(e+)]
“background-less” IBD detection?
e+
n→p-recoil
e-/α
e-/γ
LiquidO @ Chooz
PRELIMINARY

## Slide 35: 106Cd 2β+ (first) observation?
35
3 channels: 2β+(ok) ⊕ β+ε (ok) ⊕ εε (no)
Cd doped LS
e+→ difficult to mimic
2x e+→ impossible?
study: γ’s ≥ 2.6MeV
first β+β+ observation? [impossible so far]

## Slide 36: proton decay potential…
36
2 tracks: K+ and μ+
proton tracked by e+
(regardless of decay-mode)