## Slide 1
Overview of The Rare Isotope Science Project
(RISP)
Kwon Myeun
FKPPL, Jeju
May 9, 2019

## Slide 2
사업 개요 및 내용
01
사업 일반현황
1. 일반현황
사업개요 및 내용
CONTENTS
PART 1. Project Overview
PART 2. Construction Status
PART 3. System Installation
PART 4. Radiation Safety
PART 5. Summary & Outlook

## Slide 3
Part 1.
Project Overview

## Slide 4: Rare Isotope Science Project (RISP)
Providing high intensity RI beams by ISOL and IF
ISOL: direct fission of 238U by 70 MeV proton
IF: 200 MeV/u 238U (intensity: 8.3 pμA)
Providing high quality neutron-rich beams
e.g., 132Sn with up to 250 MeV/u,
up to 109 particles per second
Providing More exotic RI beam
production by combination of ISOL and IF
1. Overview
Budget: KRW 1,432 billion (US$ 1.26 billion, 1$=1,135krw)
- accelerators and experimental apparatus : 460.2 billion won
- civil engineering & conventional facilities : 972 billion won (incl. site 357 billion won)
Period: 2011.12 ~ 2021.12
Goal: To build a heavy ion accelerator complex RAON,
for rare isotope science research in Korea.
* RAON - Rare isotope Accelerator complex for ON-line experiments
Construction of research and support facility to ensure the stable operation of the heavy-ion accelerator, experiment systems, and to establish a comfortable research environment
※ Accelerator and experiment buildings, support facility, administrative buildings, and guest house, etc.
Development, installation, and commissioning of the accelerator systems that provides high-energy (200MeV/u) and high-power (400kW) heavy-ion beam
System Installation Project
Facility Construction Project

## Slide 5: RAON Layout
IF System
BIS
μSR
HPMMS/
CLS
SCL2
ISOL System
LAMPS
Cyclotron
SCL3
SCL1
ECR IS
KOBRA
NDPS
Control
Center
Utility
HRS
SCL1 has been decided to be postponed
: SCL3 is going to be taking a role of SCL1 in the early operation
1. Overview

## Slide 6
2014
2015
2016
2017
2018
2019
2020
2021
SCL demo beam
(Dec 2017)
D-1
Experiment
(Jan 2021)
18.5MeV/u
SI beam
(Dec 2020)
SCL2
(Dec 2021)
ECR-IS beam &
ISOL beam (SI beam)
(Dec 2015)
RFQ beam
(Dec 2016)
System Installation
18.5MeV/u
RI beam
(Sep 2021)
SCL
installation
(April 2019)
ISOL
Commissioning
(July 2020)
Supply of utilities
(Dec 2018)
2014
2015
2016
2017
2018
2019
2020
2021
Completion of detail design
(June 2017)
Completion of construction
(Aug 2020)
Completion of inspection of the radiation facility
(Dec 2021)
Completion of basic design
(Dec 2015)
Beginning of priority
construction
(Feb 2017)
Beginning of construction
(Sep 2017)
Building
Permit
(April 2021)
Facility Construction
(2018)
SCL3 manufacturing
SCL2 Prototype
(2019)
SCL3 Installation
SCL2 manufacturing
(2020)
SCL3 Beam Commissioning/
Const. Completion
(2021)
SCL3 Beam Commissioning/
Project Completion
Project Milestone
1. Overview

## Slide 7
Progress Rate
1. Overview
Chart: 
| End of 2011 | End of 2012 | End of 2013 | End of 2014 | End of 2015 | End of 2016 | End of 2017 | End of 2018 | End of 2019 | End of 2020 | End of 2021
Planned | 0 | 0.083 | 0.15 | 0.184 | 0.249 | 0.3046 | 0.42 | 0.6 | 0.78 | 0.91 | 1
Actual | 0 | 0.083 | 0.15 | 0.184 | 0.249 | 0.3014 | 0.407 | 0.5896
System Installation Project
As of Feb 2019
(Planned: 62.13%,
Actual: 61.19%)
2011 2012 2013 2014 2015 2016 2017 2018 2019 2020 2021
Construction Project
Chart: 
| End of 2011 | End of 2012 | End of 2013 | End of 2014 | End of 2015 | End of 2016 | End of 2017 | End of 2018 | End of 2019 | End of 2020 | End of 2021
Planned | 0.0256 | 0.0367 | 0.1312 | 0.39 | 0.67 | 0.99 | 1
Actual | 0.0256 | 0.0367 | 0.1185 | 0.39
As of Feb 2019
(Planned: 40.67%,
Actual: 40.47%)
2015 2016 2017 2018 2019 2020 2021

## Slide 8
Part 2.
Construction

## Slide 9
Building Layout
2. Construction
Building Layout
Assembly Bd.
SRF Test Bd.
High Energy B
IF Separator / High Energy A
HQ Office
Guest House
Info. Center
Cryogenics Bd.
ISOL
SCL
Utility Bd.
Electricity Bd.
Control Center
Low Energy A,B
Waste Strorage
Reservation
Campus Area : 952,066㎡ (including the reservation area of 144,640㎡)
Period : 2014 ~ 2021(8 years)
Cost : 972 billion won (incl. 357 billion won for land)
Building Area : 76,259㎡(11 Bds)
Total Bd. Area : 116,252㎡
Constructor : POSCO Consortium(11 companies)

## Slide 10
View of Construction Place
2. Construction
<`19.3>
<`17.01>
<`17.12>
<`18.6>
<Assembly Bd.>
<SRF Test Bd.>
<High Energy Exps.>
<ISOL>
<SCL3>
<Low Energy Exps.>
<Control Center>
View of Construction Place (`19.3)

## Slide 11
SCL3
Low Energy A/B
SCL2
IF/ High Energy A
High Energy B
ISOL
Conventional Facilities
2. Construction
Accelerator Bd.
SCL3
Bending Section
SCL3-gallery

## Slide 12
Assembly Bd.
Control Center
SRF Test Bd.
Utility Bd.
Electricity Bd.
HQ Office
2. Construction
Conventional Facilities

## Slide 13
Part 3.
System Installation

## Slide 14
SCL1&3(QWR)
SCL1&3(HWR)
SCL2(SSR2)
Bending Section
Injector
SCL2(SSR1)
Cyclotron
IF System
Accelerator System
3. Sys. Install.

## Slide 15
Major achievements
3. Sys. Install.
ECR 이온원
LEBT
RFQ
MEBT
QWR
Superconducting RF Test facility(2016.06)
High purity Sn beam extraction
using RILIS (2015.12)
1st Oxygen Ion beam acceleration with QWR module, SCL Demo(2017.10)
HWR cryomodule test complete
(2018.03)
QWR cryomodule test complete
(2017.05)
1st Oxygen Ion beam acceleration with RFQ(2016.12)
Achievement of low temperature test for LTS and HTS quadrupole prototype magnet (LTS 2016.1, HTS 2017.1)

## Slide 16
ISOLIF
: ISOL  SCL3  SCL2  IF
: ISOL  SCL3  KOBRA
Broad energy range, Variety, High intensity of RIBs will be available at RAON
Driver
Post accelerator
Production mechanism
Available RIB energy
SCL3
Cyclotron
SCL3SCL2
SCL3 or SCL3SCL2
Direct reactions
- (p,d), (3He,n) etc.
Multi Nucleon Transfer
p induced U fission
PF, U fission
< a tens of MeV/u
> a few of keV/u
< a hundreds of MeV/u
ISOL
IF (high E)
KOBRA (low-E IF)
RIBs at RAON
3. Sys. Install.

## Slide 17
RAON will provide access to unexplored regions of the nuclear chart
KOBRA
IF
ISOL
ISOL+IF
3. Sys. Install.
RIBs at RAON

## Slide 18
3. Sys. Install.
Nuclear science - KOBRA, LAMPS, NDPS, MMS, CLS (based on atomic physics)
Applied science - mSR (Material science), BIS (Bio & Medical application)
7 (at the beginning of RAON operation) + upgrade + ?? (in the future, space reserved)
Layout of Experimental System at RAON

## Slide 19
1. KOBRA
(KOrea Broad acceptance Recoil spectrometer & Apparatus)
2. LAMPS
(Large Acceptance Multi-Purpose Spectrometer)
∙ Research Studies of nuclear structure and nuclear
astrophysics in the energy range of < a few tens of MeV/u
∙ Current status Under fabrication (start installation from Sep. 2019)
∙ Research Studies of nuclear matter and nuclear reactions
with stable and RI beams at intermediate energy regime
∙ Current status Under fabrication (start installation from Jan. 2021)
IF separator
Current Status of Experimental System
3. Sys. Install.

## Slide 20
3. MMS (Mass Measurement System)
∙ Research High precision mass measurement of
short lived rare isotopes
∙ Current status Under assembly and test
(start installation from Feb. 2020)
MR-TOF-MS
Collaboration:
KEK/WNSC (JAPAN)
4. CLS (Collinear Laser Spectrometer)
∙ Research Model independent Studies of
nuclear ground and isomeric state properties
∙ Current status Restart development
(start installation from Jan. 2020)
5. NDPS (Neutron Data Production System)
∙ Research Measurement of neutron
induced reaction data for nuclear science
∙ Current status Restart development
6. mSR (Muon Spin Rotation/Relaxation/Resonance )
∙ Research Studies of local electromagnetic structures and
exotic properties of material by using polarized muons
∙ Current status Restart development
7. BIS (Beam Irradiation System)
∙ Research Biomedical studies such as cancer treatment,
human body effect by space radiation and cell mutation
∙ Current status Restart development
(start installation from Jan. 2021)
(start installation from Nov. 2020)
(start installation from Feb. 2021)
Current Status of Experimental System
3. Sys. Install.

## Slide 21
Facility | Subject for early phase operation
KOBRA | ∙ Transfer reaction measurements in inverse kinematics (29P(d,p)30P, 26Al(a,p)24Si) ∙ Radiative capture reactions using batch mode RI beams (26gAl(p,g)27Si) ∙ RI beam production via quasi-projectile-like fragmentation for 16O or 40Ar
LAMPS | ∙ Ar+KCl or Xe+CsI in case of IF separator commissioning not completed
MMS | ∙ Isomer separation with using 26g.s.Al and 26mAl beams
CLS | ∙ Laser ionization and measurement of isomeric property for 26Al
NDPS | ∙ Activation experiments with a quasi mono energy neutrons for light and heavy nuclei ∙ Surrogate reactions for fission
mSR | ∙ One of research areas of superconductivity and quantum magnetism with their scientific significance at the time of the μSR instrument completion
BIS | ∙ Physical dose distribution and linear energy transfer measurements with a 12C+6 beam (310 MeV/u)
Scientific program at early phase of operation
3. Sys. Install.

## Slide 22
Part 4.
Radiation Safety

## Slide 23
Radiological Features of the Facility
4. Rad. Safety
High Power Targets
Use of Uranium Material
Various Reactions to analyse
various beam and target combination
wide energy range (low 18~40MeV/u, high 200~320 MeV/u, 600 MeV p)
need to find correct simulation codes and conditions
IF : 400 kW, ISOL : 30 ~ 70 kW
induce high activation in concrete, air, cooling water, machine parts
need robust remote handling in target areas
fission products contaminate ISOL target system, IF beam dump, etc.
generation of radioactive waste containing actinides-> need a long-term storage space of the waste until ready to transfer to the national site
Experiments | Beams | Targets
IF | O, Ca, …, Kr, .., Sn, Xe, U, ~20 species | C
ISOL | p | UC
KOBRA | He, B, O, Ar, U | Be, Cu
Bio-medical | C | Fe
muSR | P | C
LAMPS | Ca, Ni, Zr, Sn | Ca,….
Neutron Exp. | p, d | C

## Slide 24
Radiation Safety Licensing : Completed!! (18.10)
Preparation
many domestic experts joined radiological analysis
facility basic design by a experienced company
Documents for Review
radiation safety report
(shielding, activation, env. Influence, RMS/PSIS,
exhaust, accident analysis, radioactive waste, etc..)
description of accelerators and experiments
details in radiological analysis (codes, input/output)
geological survey report
stability assessment of building and ground
quality assurance plan/procedures
fire hazard analysis
Extensive Reviews
NSSC
(Nuclear Safety and Security Commission)
KINS
(Korea Institute of Nuclear Safety)
License Submission
& Approval
Technical Review Request
& Review Report
Technical Detail
Inquiry & Answer
RISP
by more than 30 KINS reviewers
382 cases of answers/further assessment/correction/design improve and changes
multilevel review(KINS, NSSC, Advs..)
4. Rad. Safety

## Slide 25
Plan – First Facility Inspection
mandatory step before operation (every year after the first inpection)
check items
safety organization / manpower
record of quality assurance activity
performance of all RMS & PSIS systems
implementation of fire protection
performance of exhaust/draining/remote system
readiness of preventive and mitigative measures for possible accidents of more once in 30 years
procedures to handle radioactive wastes
etc..
’19 |  |  |  | ‘20 |  |  |  | ‘21 |  |  | 
1Q | 2Q | 3Q | 4Q | 1Q | 2Q | 3Q | 4Q | 1Q | 2Q | 3Q | 4Q
Arragned with KINS
to make 3-steps inspection
Ion Source
SCL3, KOBRA, ISOL
SCL2+IF, h.e.Exps
Safe Facility for workers & vistors & citizens !
RMS Equipments in the site | 
Environment Monitor | 12
Area Monitor | 94
Area Air Monitor | 11
Stack Monitor | 6
Hand & Foot Monitor | 11
Nuclide Analyser | 6
Paging Phone | 88
CCTV camera | 101
Emergency Stop & Alarm | 174
Vehicle Radiation Monitor | 2
4. Rad. Safety

## Slide 26
Part 5.
Summary & Outlook

## Slide 27
Accelerator
Mass production for SCL3 is under way
SCL2 is under pre-production phase
From April, 2019, installation for SCL will start from SCL3.
By the end of 2021, we will achieve
SI beams: Stable ion beams (16O, 40Ar) from ECRIS  SCL3  low E exp hall
RI beams: RIBs extraction from ISOL  re-acceleration through SLC3  low E exp hall
Stable / RI beams will be delivered to low-E experimental hall
Early phase experiments are going to be performed using KOBRA
  RIBs production at KOBRA (A<~50, beam energy < 20 MeV/u) using SI beams from SCL3
Beam commissioning starts for SCL2
Installation and commissioning for IF, LAMPS, Neutron, bio-medical and muSR
   Collaborative works with RUA (RAON Users Association) via RULC (RAON Users Liason Center)
Post RISP (2021 ~ )
Beam acceleration for ISOL  SCL3  SCL2  IF (ISOL+IF)
Beam commissioning and experiments for IF, LAMPS, Neutron, bio-medical and muSR
Ramping-up to get the 400kW beams (more than 5 yrs)
Energy upgrade to 400MeV/u (requires budget)
Summary & Outlook
4. Summary

## Slide 28
Thank you

## Slide 29
3. Sys. Install.
Schedule of Experimental System at RAON