## Slide 1: Status of RAON
NuSYM2018
Sep 10-13, 2018
Young Kwan KWON

## Slide 2: RAON: Rare Isotope accelerator complex for ON-line experiment
Low energy experimental hall B
Low energy experimental hall A
ISOL facility
SCL3
SCL2
SCL1
High energy experimental hall A
High energy experimental hall B
Providing high intensity RI beams by ISOL and IF
ISOL: direct fission of 238U by 70 MeV proton
IF: 200 MeV/u 238U (intensity: 8.3 pμA)
Providing high quality neutron-rich beams
e.g., 132Sn with up to 250 MeV/u, up to 109 particles per second
Providing More exotic RI beam production by combination of ISOL and IF
Goal: To build a heavy ion accelerator complex RAON for RI science researches
IF facility
Spallation room for future extension
○ Project period : 2011.12 - 2021.12
○ Total Budget : ~$ 1.43 billion
(Facilities ~ $ 0.46 bill., Bldgs & Utilities ~ $ 0.97 bill.) (include initial experimental apparatus)

## Slide 3: RAON Layout
IF System
BIS
μSR
HPMMS/
CLS
SCL2
ISOL System
LAMPS
Cyclotron
SCL3
SCL1
ECR IS
KOBRA
NDPS
Control
Center
Utility
HRS
SCL1 has been decided to be pended
: SCL3 is going to be taking a role of SCL1 in the early operation

## Slide 4: RISP Organization
System Integration Team
Accelerator Systems Team
Accelerator Engineering Team
RI Experimental Systems Team
Construction Management Team
Facility & Safety Management Team
Administration & Communication Team
General Affairs & Management Team
Project Planning Team
Research & Budget Mgt. Team
Risk & Schedule Control Team
International Advisory Committee(IAC)
Civil Engineering Advisory Committee
Deputy
Director
Director
Facility
Construction
Division
Administration
Division
System
Installation
Division
Project
Coordination
Department
1 department, 3 divisions, and 11 teams

## Slide 5
Project Major Milestones
2014
2015
2016
2017
2018
2019
2020
2021
SCL demo beam
(Dec 2017)
D-1
Experiment
(Jan 2021)
18.5MeV/u
SI beam
(December 2020)
SCL2
(Dec 2021)
ECR-IS beam &
ISOL beam (SI beam)
(Dec 2015)
RFQ beam
(Dec 2016)
Facility
18.5MeV/u
RI beam
(September 2021)
SCL
installation
(April 2019)
ISOL
(July 2020)
Supply of utilities
(October 2018)
2014
2015
2016
2017
2018
2019
2020
2021
Completion of detail design
(June 2017)
Completion of construction
(Dec 2020)
Completion of inspection of the radiation facility
(Dec 2021)
Completion of basic design
(Dec 2015)
Beginning of priority
construction
(Feb 2017)
Beginning of construction
(Sep 2017)
Building
Permit
(April 2021)
Construction & Civil Engineering

## Slide 6: Construction
Feb, 2017
May, 2017
Aug, 2017
Dec, 2017
Mar, 2017
Aug, 2017

## Slide 9: Lineup of RIB production & Separation
ISOL
IF (high E)
KOBRA (low E IF)
Driver
Post acc
Production mechanism
Available RIB energy
SCL3 or SCL1
Cyclotron
SCL32 or SCL12
SCL3 or SCL32
Direct reactions
- (p,d), (3He,n) etc
, MNT
p induced U fission
PF, U fission
< a tens of MeV/u
> a few of keV/u
< a hundreds of MeV/u
ISOLIF
: ISOLSCL3SCL2IF
: ISOLSCL3KOBRA
IFRe-Acc
: IFstopped beamSCL
(future upgrade)

## Slide 10: RAON Layout : Accelerator System
SCL1&3(QWR)
SCL1&3(HWR)
SCL2(SSR2)
Bending Section
Injector
SCL2(SSR1)
Cyclotron
IF System

## Slide 11: ECR Ion Source(28GHz, 14.5GHz)
2011 ~ 2014
~ 2019.06
~ 2019.12
2020
Design & Fabrication
Installation & Test (Munji Campus)
Transfer to main site
Commissioning
2021
Operation
28GHz
2018
~ 2019
~ 2020.5
Purchasing process
Manufacturing
Installation & Commissioning
2020.6~
Operation
14.5GHz
28GHz ECR test results
 As an early test stage,
- O7+ of 30euA was extracted
- Ar11+ of about 70euA was extracted.
 After cryo-cooler maintenance,
cooling capacity margin is improved.
 14.5GHz ECRIS for a secondary ion source.
 14.5GHz ECRIS and 28GHz ECRIS will supply a stable isotope beam to SCL3 alternately
 14.5GHz ECRIS will be a main ion source when 28GHz ECRIS moves to SCL1

## Slide 12: Injector
 Completion of RFQ manufacturing and tuning (Quad. Field < 2%, Dipole Field < 5% of Q.)
 Installation of injector and test for beam acc. Performance of RFQ (>500keV/u)
RFQ at SCL DEMO
<RFQ tuning result>
2011 ~ 2012
~ 2015
~ 2018
2019
Conceptual design
Prototype
Test & Upgrade
Installation
2020
Commissioning
2021
Operation
Installation & Test of injector @ SCL demo
<Energy spectrum of beam from RFQ>

## Slide 13: SuperConducting Linear accelerators (SCL3, SCL2)
Superconducting cavity test
 SRF test facility @ KAIST Munji Campus
 Manufacturing and Performance test for QWR x 4, HWR x 6, SSR1 x 1 is under way (‘18)
<Result of HWR cavity performance test>
<Cavity test pit, Cryostat, Control room>
2011 ~ 2012
~ 2016
~ 2018
2019
Conceptual design
Prototype
Test and Manufacturing
Installation
2020
Commissioning
2021
Operation
SCL3
(QWR, HWR)
2011 ~ 2012
~ 2018
~ 2019
~ 2021
Conceptual design
Prototype
Test and Manufacturing
Installation & Commissioning
2022
Operation
SCL2
(SSR1, SSR2)
QWR
HWR
SSR2

## Slide 14: RAON Layout : RI & Experimental System
Low Energy Exp. Bldg
Ultra-low Exp. Bldg
High Energy Exp. Bldg
CLS
HPMMS
Neutron Facility
KOBRA
Bio-medical facility
mSR
LAMPS
ISOL
IF

## Slide 15: ISOL System
2011 ~ 2012
~ 2017
~ 2019.3
~ 2020.7
Conceptual design
Prototype
Manufacturing
Installation
2021.6
Commissioning
2021
Operation
System | Specification | Current Status | 
Target Ion Source | ㆍUCx Fission Target 10kW ㆍSIS, RILIS, FEBIAD | ㆍManufacturing(partly) | 
Beamline, Remote handling, Hot cell System (incl. A/q Separator) | ㆍRA/q : ~200 (for EBIS) ㆍE + B Combination | ㆍPurchasing process | 
RFQ cooler & Buncher | ㆍCooling time : <100 ms ㆍTransmi. Effi. : >50%(Sn) ㆍOutput emittance: <3 ㆍCapacity: <108 ions/bunch | ㆍUnder design | 
EBIS-Charge Breeder | ㆍE/A : 10 keV/u ㆍA/q : 10 keV/u ㆍEffi. : 15%(133Cs27+) ㆍBreeding time: 50~100 ms ㆍCapacity: <108 /bunch | ㆍStart integrate assembling - E-gun/collector - SC solenoid - Drift tube ㆍBreeding test (‘18.12~) | 

## Slide 16: IF System
2011 ~ 2012
~ 2018
~ 2020.11
~ 2021.7
Conceptual design
Prototype & Test
Manufacturing
Installation
2021.12
Commissioning
2022~
Operation

## Slide 17
2011 ~ 2012
~ 2017.9
~ 2019.4
~ 2020.12
Conceptual design
Prototype & Test
Manufacturing
Installation & Commissioning
2021.1~
Operation
KoBRA (KOrea Broad acceptance Recoil spectrometer and Apparatus)
Stage 1
A first part of stage1 (stage1 part1) has been contracted with foreign and domestic companies in April 2018, and production is ongoing.
The present design of second part of stage1 (stage1 part2) was finally decided among the various design options in June 2018 by consultation with domestic potential users, and is scheduled to bid in August 2018.
Stage1 will be installed in Low Energy Experimental room (E1) until the end of June 2020.
The commissioning of Stage1 will be started from beginning of 2021 with stable ion beam.
PPAC
- We have 2 10 x 10 cm2, 2 20 x 20 cm2, 1 40 x 20 cm2 active area PPACs
- 4 10 x 10 cm2 and 1 40 x 20 cm2 PPACs will be produced
SSD
- We have 2 5 x 5 cm2 active area, 50 m thick, 16 channel SSD
- Energy resolution ~ 0.7%, S/N ~ 272 for 5.486 MeV  inside vacuum
Plastic scintillator detector
- We have 2 10 x 10 cm2 active area, 100 m thick both side readout
plastic detector
- Time resolution < 42 ps for 5.486 MeV  inside vacuum

## Slide 19
2011 ~ 2012
~ 2018.12
~ 2020.12
~ 2021.7
Conceptual design
Prototype & Test
Manufacturing
Installation
2021.12
Commissioning
2022~
Operation
LAMPS (Large Acceptance Multi-Purpose Spectrometer)
Beam Energy: up to 250 MeV/u
Solenoid Spectrometer
- Max. 1T solenoid magnet
- TPC (~ 3 sr acceptance, charged particle tracking)
- Scintillation counter (trigger & ToF)
Neutron Wall (neutron tracking)
Design change
- Normal to superconducting magnet
- Coil radius: 1 m  0.8 m
- Fulfill requirement
operation B-field: 0.5 T
maximum B-field: 1 T, B/B < 1% at Time Projection Chamber region
Solenoid Magnet
Forward Neutron Detector Array
- Completed all R&D processes
- Finalized Array frame design
- Detector production in progress
2 veto detectors (total: 20)
10 neutron detectors (total: 160)
- Complete integration & test by the middle of 2019
Time Projection Chamber (TPC)
- Test with prototype of TPC completed
- Fulfill the requirement of TPC
- Based on test results, change TPC design
Both side readout  one side readout
P-10 gas  P-20 gas

## Slide 20: High Precision Mass Measurement System (MR-TOF)
2011 ~ 2012
~ 2020.1
~ 2020.10
~ 2021.12
Conceptual design
Manufacturing & Test
Installation
Commissioning
2022~
Operation
MRTOF-MS construction under the collaboration
R&D work, led by WNSC MRTOF group (Leader : Prof. Wada)
Additional beam line to the MRTOF-MS, already constructed (2017)
Differential pumping system, gas cell (or catcher), Trap system, and MRTOF analyzer have been assembled, waiting for offline ion source test.
Test of the differential pumping system with the gas cell filled with 1 mbar helium gas, performed : 3.4x10-4 Pa upstream side (acceptable)
Optimizing the beam transmission through the φ 2-mm gas cell hole, performed : 72% efficiency, but will be improved by additional beam steerer.
A picture of MRTOF-MS system and others
at RISP-KEK/WNSC
Gas cell (catcher)
Trap system

## Slide 21: Summary & Outlook
Accelerator
Mass production for SCL3 is under way
SCL2 is under pre-production phase
From April, 2019, installation for SCL will start from SCL3
Test facility for cavities and cryomodules will operate from next Jan.
By the end of 2021, we will achieve
SI beams: Stable ion beams (16O, 40Ar) from ECRIS  SCL3  low E exp hall
RI beams: RIBs extraction from ISOL  re-acceleration through SLC3  low E exp hall
Stable / RI beams will be delivered to low-E experimental hall
Early phase experiments are going to be performed using KOBRA (with low intense RI beams)
  RIBs production at KOBRA (A<~50, beam energy < 20 MeV/u) using SI beams from SCL3
Beam commissioning starts for SCL2
Installation and commissioning for IF, LAMPS, Neutron, bio-medical and muSR
   Collaborative works with RUA (RAON Users Association) via RULC (RAON Users Liason Center)
Post RISP (2021 ~ )
Beam acceleration for ISOL  SCL3  SCL2  IF (ISOL+IF)
Beam commissioning and experiments for IF, LAMPS, Neutron, bio-medical and muSR
Ramping-up to get the 400kW beams (more 5 yrs)
Energy upgrade to 400MeV/u (require budget)

## Slide 22
Thank you