## Slide 1
Vibration monitoring and analysis in SuperKEKB M. MAZUSAWA1, H. YAMAOKA1, P. BAMBADE2, G. BALIK3, L. BRUNETTI3, S. DI CARLO2, A. JEREMIE3 , M. SERLUCA3 1: KEK, High Energy Accelerator Research Organization, Tsukuba, Japan
2: LAL, Laboratoire de l'Accélérateur Linéaire, Orsay, France
3: LAPP-IN2P3-CNRS, Université de Savoie Mont Blanc, Annecy, France
Joint workshop of TYL/FJPPL and FKPPL, Jeju, 9-11 May 2019
http://nuclear.korea.ac.kr/indico/conferenceDisplay.py?confId=395
Notes: 5/10/19
Entrez votre nom
1

## Slide 2
  Contents
  Description of our proposal (A_RD_14)
  SuperKEKB site
  Status
    Experimental setup
      Preliminary measurements
      1st observation
      Modelling
      Hardware upgrade
    Summary( Schedule& Budget : 2019)
Vibration monitoring and analysis in SuperKEKB

## Slide 3
3
Target:
  Measure the vibration due to the seismic activities and the cultural noise, near the IP.
  Check a correlation between vibration and luminosity when with/without the collision orbital feedback running.
Procedure:
  4 seismic sensors (Guralp 6T) running real time (a few minutes / hour) 24 hours a day, on a large bandwidth [0,1 – 100] Hz in vertical and horizontal directions
Location:
  Two sensors at each side of the Belle II detector. One (A) as close as possible to the IP and one (B) along the collider which could be moved time to time for coherence monitoring / diagnostic in time..
Description of our proposal
IP

## Slide 4
4
Description of our proposal
Status:
  Two visits to KEK (two persons per visit) during the last year.
  Two sensors, one each side of the IP, are installed.
  Data have been taken. Access from France has become possible.
  Data analysis being done.
Schedule:
  Continuation of measurements and modelling of the vibration of each magnet in the cryostat.
  The setup will be upgraded during next year.
Budget:
  Last slide
There are 4 quadrupole magnets and many correction magnets in a cryostat. Do all quads vibrate coherently when cryostat vibrates?

## Slide 5
A_RD_14
SuperKEKB site
Not quiet at all

## Slide 6
Not quiet at all
SuperKEKB site

## Slide 7
7
Description of the installed setup:
Experimental Setup
1 :The sensors were used at ATF2 experiment at KEK originally and now they are moved to SuperKEKB tunnel.
2 The DAQ real time National Instruments is lent by the LAPP mechanics department for one year.
 | Designation | Characteristics
cRIO 9022 | Real-Time Embedded Controller | 533 MHz, 2GB storage, 256 MB DRAM
Chassis Ni 9114 | Virtex-5 LX50 FPGA CompactRIO Chassis | 8-Slot
Module NI 9239 | C Series Voltage Input Module (x2) | 2x4 analog channels +/- 10V, 24 bits, upt to 50 kHz
Geophones | 4 seismic sensors CMG-6T | 30 s – 100 Hz, 2 × 1200 V/m/s
Real time measurement National Instrument setup
Seismic sensor
Guralp 6T
Sensors power supply and signal conditioning
Labview:
Monitoring & logging
Remote
access
1
2

## Slide 8
Preliminary measurements (November 2018)
PSD
Coherence in vertical and transversal directions
Measurements carried out at the both sides of the IP to check coherency
IP
1 10 100(Hz)

## Slide 9
Preliminary measurements (November 2018)
LAPP sensor “health” checkup
Comparison between LAPP & KEK : Data taken on the Cryostat for final focus superconducting quadrupole magnets
A
B
C
D
KEK
KEK
LAPP
LAPP
Measurements on the cryostat (LAPP)
Horizontal
Vertical

## Slide 10
Installation (February 2019)
The sensors are placed inside a box made of lead and mu-metal, for protection from radiation, magnetic field and human activities during the machine maintenance.

## Slide 11
First observations
Example: irregular (not permanent) peaks (1.6Hz)
19th April
PSD of displacements : observed peak at 1.4 Hz
Comparison between the luminosity and vibration started
Mysterious peak
Source identified?

## Slide 12
KEK
https://www.pwri.go.jp/eindex.html
Large dynamic centrifugal load test equipment
1.36 Hz
1.38 Hz
1.64 Hz
1.69 Hz
Vibration peak frequency matched with
spinning frequency (→centrifugal load).
f=mrw2
https://www.youtube.com/watch?v=b-kNqO-ohwA

## Slide 13
Modelling (KEK):
21Hz
23Hz
42Hz
The objective is to complete the initial model done by KEK to estimate the final focusing magnets inside the cryostat in function of the measured vibrations on the ground (particularly the differential motion between the focusing magnets)
2019 - Modelling

## Slide 14
2019 - Modelling

## Slide 15
2019 - Hardware upgrade
 | Designation | Characteristics
cRIO 9056 | Real-Time Embedded Controller | 533 MHz, 2GB storage, 256 MB DRAM
Module NI 9239 | C Series Voltage Input Module (x2) | 2x4 analog channels +/- 10V, 24 bits, upt to 50 kHz
cRIO new generation
The current cRIO is almost no longer commercialized by NI
The initial setup has allowed to start the experiment in time. The final one will be suitable to the long term schedule of the project
The budget is supported by LAPP.
CompactRIO (or cRIO) is a real-time embedded industrial controller made by National Instruments for industrial control systems. The CompactRIO is a combination of a real-time controller, reconfigurable IO Modules (RIO), FPGA module and an Ethernet expansion chassis

## Slide 16
16
Summary
Data acquisition started.
Remote access to the system from LAPP has become avaiable.
Data are taken during SuperKEKB Phase 3 run.
During the summer shutdown, we plan to do the followings:
  Upgrade of the system
  Data taking of the cryostat vibration when cryostat is pushed back for its maintenance.
  Modelling of the each quadrupole magnet in the cryostat using the cryostat data.
2019l budget of the project:
FJPPL request:
Hardware: new system (5K)
Missions on site (2 persons)
Total about 11 Keuros
Missions on site (2 persons)
Total 6 Keuros