## Slide 1: Direction-sensitive dark matter detection with gaseous tracking detectors (new proposal / D_RD_21)
Kentaro Miuchi
(KOBE University) CoｰPI:Daniel Santos (LPSC/IN2P3)
@ 2019 Joint workshop of FKPPL and TYL/FJPPL

## Slide 2: Physics case : dark matter
    ～1/4 of the universe
    (can be) unknown particle beyond standard model direct search: DM-nucleus interaction
GC
Our GALAXY （dark matter “HALO”）
SUN
constellation “CYGNUS”
nucleus
nucleus
DM
SIGNAL ER<～100keV
@ lab (direct search)
the universe
(energy pie chart)

## Slide 3
nucleus
nucleus
DM
SIGNAL ER<～100keV
    expected direct DM signals
    ① observed * events ② energy spectrum
    ③ seasonal modulation
    ④ material dependence
    ⑤ direction-sensitive
    DM direct search

## Slide 4
    “direction-sensitive” dark matter direct search
    detect the direction of the recoil nuclei
GC
Our GALAXY
SUN
constellation “CYGNUS”
nucleus
nucleus
DM
SIGNAL ER<～100keV
@ lab
    forward recoil would be a “smoking-gun” evidence
cosθ
1
-1
0
0
20
40
M=80GeV
σ=0.1pb
[count/3m3/year/bin]
directionality (expected)
θ
θ

## Slide 5: proposal overview
    Title：Direction-sensitive dark matter detection with gaseous tracking detectors
    Plan: 2019-2020 detector calibration @ Grenoble 2020- Dark matter search @ Kamioka
    Member：Japan Kentaro Miuchi（Kobe）（PI）
    Kiseki Nakamura, Tomonori Ikeda, Hirohisa Ishiura, Takuma Nakamura, Takuya Shimada （Kobe）
    France Daniel Santos (LPSC/IN2P3) (PI) Charling Tao (CPPM/IN2P3), Fabrice Naraghi, Olivier Guillaudin, Jean-François Muraz (LPSC/IN2P3)
    Funding request (2019-2020)： Japan 1700k \ France 5k €

## Slide 6: Background
Miuchi and Santos are leading two major direction-sensitive experiments: NEWAGE and MIMAC
  Both use MPGD (micro-patterned gaseous detectors)
  No co-working before
m-PIC (400mm pitch)
direction-sensitive limit
Underground
MIMAC
Moderne underground
30cm
10cm
25cm
40cm
NEWAGE
Kamioka underground
PTEP (2015) 043F01s

## Slide 7
We are in the same “CYGNUS” community.
Bi-annnual workshop 2007-
This TYL/FJPPL would be a good kick-off for a important collaborative work.

## Slide 8
pre-works
  2×review papers

## Slide 9: NEWAGE: 3D-tracking
μ-PIC(MPGD) based TPC
  3-D tracks SKYMAP
CF4 gas for SD search
Proposal PLB 578 (2004) 241
First direction-sensitive limits
  PLB654 (2007) 58
Underground results
PLB686 (2010) 11, PTEP (2015) 043F01s
Phase for “low BG detector”
New general WIMP search with an Advanced Gaseous tracker Experiment
SKYMAP (measured DATA)
30cm
40cm

## Slide 10
Expertise of MIMAC: COMIMAC
J.F. Muraz, J. Médard, D. Santos et al., NIMA 832 (2016), 214

## Slide 11
  COMIMAC measures Quenching Factor (nuclear tracks ionize less effectively than electron tracks) ⇒important as a “calibration ” for a DM detector
QF=0.25
QF=0.36

## Slide 12
Chart: Ionization Quenching Factor for Fluorine in pure CF4 at 50 mbar and for 4He in helium (D. Santos et al.)
| 20 | 10 | 5 | 7 | 7 | 50 | 40
Fluorine in CF4 at 50 mbar | 0.37237 | 0.30498 | 0.25696 | 0.27866 | 0.27497 | 0.47061 | 0.45287
He in He + 5% C4H10 at 350 mbar | 0.65703 | 0.66705 | 0.66705 | 0.7043 | 0.61942 | 0.617 | 0.59206 | 0.54493 | 0.62367 | 0.73686 | 0.75767 | 0.76932 | 0.52057 | 0.51955 | 0.47032 | 0.42392 | 0.55031

## Slide 13
Expertise of NEWAGE: Negative-Ion TPC
  original study by New Mexico group
  readout electronics development by NEWAGE
  intensive SF6 gas study
several species of ions with different velocities
z-fidutialzation → Background killer!
2017 JINST 12 P02012
NEWAGE Background schematics
averaged waveform (Tomonori Ikeda)

## Slide 14
  NEWAGE electronics for SF6
2019 J. Inst. 14 T01008
Kobe-KEK(Liq Ar group) ASIC development
first-ever detected 3D tracks in SF6 gas

## Slide 15
This proposal ① (2019-2020):
＋
averaged waveform (Tomonori Ikeda)
  19F quenching factor measurement @ LPSC Grenoble low energies (1-50 keV) low pressure SF6 gas

## Slide 16
This proposal ② (2020-) :
＋
CYGNUS/NEWAGE multi-window chamber
  direction-sensitive dark matter search @ Kamioka
MIMAC low background MIcromegas

## Slide 17: Summary
New Proposal: Direction-sensitive dark matter detection with gaseous tracking detectors
By Miuchi (NEWAGE leader) and Santos (MIMAC leader)
QF measurement (2019-2020)
Dark Matter Search (2020-)

## Slide 18: BACKUPS

## Slide 19: low pressure gas TPCs
NEWAGE
[Kobe+]
m-PIC (400mm pitch)
direction-sensitive limit
Underground
Micromegas (~400mm pitch)
quenching factor measurement
Underground
MWPC (2mm pitch)
First started direction-sensitive method
Underground
Low background
Large size (1m3)
1m
MIMAC [France]
DRIFT
[UK+US]
D3 [Hawaii]
30cm
10cm
2cm
10cm
50cm
25cm
40cm
pixel/optical
NITEC/CYGNO [Italy]
Pixel readout (ATLAS FE-I4) chip
R&D in the surface lab
Notes: In order to get nuclear track, it is usual to use Time Projection Chamber (TPC).
This is schematic image of TPC.
First, dark matter interact to nuclear.
And then, nuclear run in the gas ionizing around gas molecular.
Ionized electrons are dragged to MPGD by electric field.
MPGD detect 2-dimensional projection of track.
And using the time electron reached to MPGD, we can get another 1-dimensional information.
Thus, TPC detect 3-dimensional nuclear track.
Typical length of nuclear track scattered by dark matter is about 1cm.
So, MPGD is suitable for direction-sensitive dark matter search.
By the way, information of nuclear track have another advantage.
The length of nuclear event is short but electron events recoiled by Compton scattering is long.
If we know track length, we can discriminate gamma-ray event from nuclear event.
This graph is detection efficiency of electron events.
Using MPGD, detector have gamma ray rejection power.

## Slide 20
T.Ikeda JPS Sep ２０１７

## Slide 21: 物理目的：稀事象実験
    2017年 ”COHERENT” 実験によって初検出。
    かならずある反応。 例えば太陽から。
    応用例② ニュートリノ-原子核コヒーレント散乱
solar
atmospheric
ecliptic coordinate
10B
WIMPS
expected

## Slide 22: “CYGNUS” physics after discovery
Test the DM motion
  ex. Sagittarius stream
  streams, halo model…
standard HALO
standard HALO + stream
GC
Our GALAXY
SUN
constellation “CYGNUS”
Sagittarius stream
galactic coordinate
expected

## Slide 23: “CYGNUS” physics after discovery
Test the interaction by scattering angle
  some operators are distinguishable
SI
SD

## Slide 24: “CYGNUS” physics after discovery
Test the interaction by scattering angle ②
  iDM (inelastic scatterings dark matter) and normal darkmatter ( FFeDM (form factor elastic dark matter)) show different angular DISTRIBUTION