## Slide 1: Status of LAMPS Time Projection Chamber
이효상
LAMPS kick-off meeting
2018.07.31

## Slide 2
Concept of LAMPS TPC
LAMPS
Solenoid spectrometer
Neutron detector array
Solenoid magnet
Target
TPC
ToF
Time Projection Chamber (TPC) - main detector for tracking of charged particles - inside of Solenoid magnet - complete information of momentum & PID - Gas Electron Multiplier (GEM) - FrontEnd electronics : GET system
Outer Field Cage
Inner Field Cage
Readout PAD
Triple GEM
Gas volume
Cathode
120cm
Target
30cm
15cm
50cm

## Slide 3
History of LAMPS TPC R&D
LAMPS
Small GEM test - GEM gain test : Fe55 & Cosmic-ray muon - reduced CoBo system
Prototype TPC test - prototype TPC design and making - muon test : drift velocity - positron beam test : drift velocity, diffusion and position resolution - CoBo system with Narval DAQ
Large GEM test - similar size of LAMPS TPC GEM - modified CMS GEM - GEM gain - gain uniformity - gain as gas - gain as number of GEM layers

## Slide 4
Small GEM gain test
LAMPS
GEM gain-voltage characteristic of Triple GEM (2mm)
Fe55 source
5.9keV
Triple GEM

## Slide 5
Bottom to fix PAD & GEM : Al
Inner Field Cage
Outer Field Cage
Cathode
GEM : 3 layers
PAD
150 mm
Drift length : 570 mm
490 mm
1/8 volume of real TPC design
Prototype TPC for LAMPS
LAMPS
Field Cage
Concept of prototype TPC for LAMPS
Optimized design & fabrication method : 1/8 volume of real TPC Honeycomb body for gas chamber
PAD : 3x10 mm2, 4x15 mm2
GEM : GEM gain test, produced by Korean company (MECARO)
Field cage : Uniform electric field by cu strip
Readout system : GET system
Analysis : Development of reconstruction algorism
3x10
357ch
4x15
175ch
Readout PAD

## Slide 6
Trigger counter 1
Plastic scintillators
1cm x 1cm
Trigger counter 2
Plastic scintillator
4cm x 4cm
Electronic & DAQ
Trigger logic
VME DAQ
TPC readout
GET system
m-TCA
AsAd board
TPC
HV system
PNC 3500 (GEM)
PNC 60000 (FC)
ELPH beam test setup
ELPH Beam test

## Slide 7
m-TCA
1CoBo + 4AsAd
Low Voltage for AsAd
Gas flow meter
TPC readout system
ELPH Beam test
AsAd board
Small test chamber with 3x10 PAD
Run summary
- beam time : 2days (12h+12h)
- positron beam
- beam height @ TPC
: 20.24cm, 35.24cm, 50.24cm
- test gas : Ar-CH4(90:10), Ar-CO2(90:10)
- Electric field of FieldCage
: 115, 125, 135, 145, 155V/cm – P10
170V/cm – ArCO2
- Operating HV @ GEM : 345V

## Slide 8
Trigger logic
- Coincidence of 6 trigger counters
- monitor trigger counting @ control room
VME DAQ for trigger counter ADC
V792N
Trigger system
ELPH Beam test
Trigger 1
Trigger 2
Trigger 3
Trigger 4
Trigger 5
Trigger 6
Linear Fan out
LED
Coin.
Level=2
Coin.
Level=4
Coin.
Level=4
20ns delay
CoBo0,1
Fan In/Out
-1
Trigger output pulse
Gate Generator
Gate Generator
Fan In/Out
+1
Linear Fan out
Veto
AsAd 1,2,3,4,6
Fan In/Out
-1
busy out
VME
V792N
GG8020
External trigger in
Gate : width=200ns
Delay signal : 100ns
Analog
NIM
TTL
LAMPS TPC prototype

## Slide 9
Event display
LAMPS TPC
Raw signal
X vs Y
Z vs Y
50.24cm
35.24cm
20.24cm
X @ front
X @ rear
X position
@ front
@ rear
Track direction
Time Bucket (ch)
ADC

## Slide 10
Drift velocity as TPC electric field
P10 : 5.25 cm/ms @ 155 V/cm
P20 : 6.77 cm/ms @ 205 V/cm
ArCO2 : 1.06 cm/ms @ 170 V/cm
Drift Velocity
Test result
Measurement of Drift velocity
ELPH Beam test - Beam height : 20.24cm, 35.24cm, 50.24cm - Gas : Ar-CH4(90:10), Ar-CO2(90:10) - Electric field 115V/cm ~ 155V/cm for Ar-CH4(90:10) 170V/cm for ArCO2
Cosmic-ray muon test - trigger counter : 4cm & 20cm - Gas : Ar-CH4(90:10), Ar-CO2(80:20) - Electric field 155V/cm ~ 175V/cm for Ar-CH4(90:10) 155V/cm ~ 205V/cm for Ar-CH4(80:20)
Drift Time distribution as beam height @ ELPH test
Time Bucket (ch)
Counts

## Slide 11
Diffusion
= +
: standard deviation of charge cloud
: transverse diffusion
: from readout system
P10 : 420 @ 155 V/cm
Test result

## Slide 12
Position resolution
Test result
3x10 mm2 PAD
4x15 mm2 PAD
Resolution : 513mm
Resolution : 228mm
e+

## Slide 13
Large GEM test
LAMPS
Large GEM
Leakage current measurement
PAD
PAD
Large GEM test bench

## Slide 14
Large GEM test
LAMPS
Fe55 event
muon event

## Slide 15
Large GEM test
LAMPS

## Slide 16
Summary
LAMPS TPC
  To study the symmetry energy in the EoS of nuclear matter
  Main detector for tracking of charged particles inside of solenoid magnet
  Complete information of Momentum & PID
Prototype TPC
  1/8 volume of LAMPS TPC
  Triple GEM system
  Readout system : GET system
  ELPH beam test
  Cosmic ray muon test
Test result
  Drift velocity P10 : 5.25 cm/ms @ E=155 V/cm P20 : 6.77 cm/ms @ E=205 V/cm ArCO2 : 1.06 cm/ms @ E=170 V/cm
  Diffusion P10 : 414 @ E=155 V/cm
  Position resolution 3x10 mm2 PAD : 228mm 4x15 mm2 PAD : 513mm
Plan
  Large GEM test
  LAMPS TPC design