## Slide 1: Current status of LAMPS neutron detector cosmic ray data analysis
Lee Jong-won

## Slide 2: Cosmic ray data taking
Feb. 17th – Mar. 30th
Total data size : 8.1TB
Run number : 401 – 567, 1 run/4 hr
Total data taking duration : 665 hr
Using 3 layers of neutron detector
Avg 4 kHz Trigger rate.
Dep E of MIP is 20 MeV.
20 MeV = 500mV( = 1000 count )
Energy calibration is done with Charge of signals.
Timing calibration is done with vertically penetrated events.
P5
P4
P3
P2
P1
P0
780 mm
2000 mm

## Slide 3: D offset alignment
D offset = Position
Position alignment methods
  Edge finding : Find edge & get offsets
  Track fitting : Fit event with line & get offsets
Tl
Tr
Toff= (Tr + Tl)/2

## Slide 4: S offset alignment
Timing of detector : Ti = (Tr+Tl)/2
Timing offsets exist for every case.
  Time stamp difference between FADC channels
  Cable length
  PMT signal speed
Dij = ti-tj
Offset : Oij
Sigma : Sij
Distribution of sigma (Sij dist. for i, j)
Layer 1
Layer 2
Layer 3
Mean value of Sigma : 181 ps -> Expected Timing resolution(FWHM) = 301 ps

## Slide 5: Simple method for t cal
grX[i](j) = Ai-Bj –(Ai-B9)
grY[i](j) = Aj-Bi–(A9-Bi)
After Offset subtraction, Oij distribution was aligned to 0, with 20 ps deviation
Offsets between two modules in diff. planes
Before Offset subtraction(Oij dist)
After Offset subtraction
Black : layer 1
Red : layer 2
Green : layer 3

## Slide 6: Energy calibration
MIP peak = 20 MeV

## Slide 7: What I want to see was…
P5
P4
P3
P2
P1
P0
Stopped at p1
Proton penetrated 4 planes and..
or
P5
P4
P3
P2
P1
P0
Leaves two hits on NDA
Neutron? hits p4 or p5 and

## Slide 8: What I saw
Deposit E on P1 vs T1-T5
High beta particle
Some particle stopped at p1
Cut condition : P1-5 have single hits. No req. on P0.

## Slide 9: Time diff distribution
Up going particle?
T1-T5 (before offset adjust)
11ns ~ 1.65m x2

## Slide 10: Analysis 25 run ( 100 hr ) data with tight cut
Cut condition
  P1-5 had single hit.
  Dep. E on P2-4 > 15 MeV
  Abs( x,y ) < 0.9 (fiducial cut)
  Hit position on P3 is on the track ( distance < 5 cm )

## Slide 11
Dep. E on P1 vs beta(p1-p5)
Dep. E on P0 vs beta(p1-p5)
Dep. E on P5 vs beta(p1-p5)
Two slow particles
No particles
with beta < 0.5
Two tails
There were two peak-like structure.
No particle found under beta < 0.5( particle was stopped at p1 )
Two tails
  Slow particle with high energy loss(kaon??)
  Fast particle with MIP energy loss (pion, muon)
Check with bethe-bloch equation

## Slide 13: Upgoing particle…
23 events