## Slide 1: Beam Diagnosis System
Seonghak Lee, Hyunchul Kim, Dong Ho Moon,
Sanghoon Hwang
Chonnam National University, KRISS
2020/05/15 LAMPS Collaboration Meeting

## Slide 2: News from CNU
Clean room installation : next Tuesday
  Hard type 1500 mm x 1500 mm
    Cleanliness class 1000 same as KRISS requirement
    Price : 5556000 won
  Purchase of Equipment to construct
Reopen KRISS from next week
  Jaein will visit and restart wiring
To do list
  Purchase of Gas (P10) and regulator
  Making chamber frame and spacer
  Test trigger system
BDC
Plastic Scintillator
Plastic Scintillator
PMT
PMT

## Slide 3: LAMPS 3D (이형준 학생 작품)

## Slide 4: LAMPS 3D (이형준 학생 작품)
Vacuum chamber

## Slide 5: LAMPS 3D (이형준 학생 작품)
Solenoid

## Slide 6: LAMPS 3D (이형준 학생 작품)
Neutron Detector (V : Veto, N : Neutron detector)
  VNNNN (Current design)
  VNVNVNVN
  VNNVNN

## Slide 7: 전시 모형 만들기, 생각해 볼 것들
빔라인 TPC 까지만 만들 것인가?
Target 위치
TOF 는 제대로 구현되었는가?
중성자 검출기 최종 시나리오는 ? VNNVNN or VNVNVNVN
Anything else?

## Slide 8: Summary & Plan

## Slide 11: Get Yield of 136Sn by LiSe++
In order to verify if our understanding would be correct or not, we reproduced yield of 136Sn by LiSe++
BigRIPS results : Y. Shimizu et al., JPSJ 87 (2018) 014203

## Slide 12: Get Yield of 136Sn by LiSe++
Results
Sn
Not same but similar order of magnitude for the yield of 136Sn

## Slide 13: Beam Size Study
Final observed beam size : x (-1.4 ~ 1.2 cm) and y (-1.2 ~ 1.2 cm)
Possible to trace 136Sn beam step by step

## Slide 14: SMURAI Detector

## Slide 15: Beam Profile Detector in SMURAI

## Slide 16: SMURAI BDC (Beam Drift Chamber)
NIMB 317 (2013) 294-304
Walenta type Drift chamber
2.5 mm drift length
i-C4H10 at 50-100 torr
Anode, potential wire diameter of 20 μm(Au-W), 80 μm(Au-Al)
Cathode (gas window) 8 μmt Al-Kapton
Effective area : 8 cm x 8 cm

## Slide 17: SMURAI BDC (Beam Drift Chamber)
NIMB 317 (2013) 294-304
Walenta type Drift chamber
2.5 mm drift length
i-C4H10 at 50-100 torr
Anode, potential wire diameter of 20 μm(Au-W), 80 μm(Au-Al)
Cathode (gas window) 8 μmt Al-Kapton
Effective area : 8 cm x 8 cm
Requirements
Position resolution : ~ 100 μm
Efficiency : 100 % at > 600 V

## Slide 18: SMURAI BDC (Beam Drift Chamber)
Beam Rate Estimation : LiSe++ (Seonghak Lee)
  Expected Beam : 132Sn : 8 x 10+6 pps with 133.2 MeV/u
To determine specific conditions of Drift Chamber, we will use GarField program (Dr. Hwang with Seonghak Lee)

## Slide 19: BDC Construction
Prototype Design
Configuration : xx’yy’ (4 planes)
Sensor Wire : 32ch
Potential Wire : 33ch
Drift Length : 2.5 mm
32 * 2.5 * 2 = 160 mm
Active Area : 160 x 160 mm2

## Slide 20: BDC Construction
NIM Crate & Power Supply & SH Cable
Place for wiring

## Slide 21: Beam Study with LiSe++
Simple layout
Beam size at L-Target (x)
: ± 4.2 mm
124Xe (260 MeV/u) Beam and14C target

## Slide 22: Beam Study with LiSe++
Comparison of Distribution Method and MC Method
  Distribution method : fast analytical method to calculate the fragment transmission through all optical blocks of the spectrometer.
  MC method : developed for a qualitative analysis of fission fragment kinematics and utilized in the Kinematics calculator. (random event generation one by one)
Distributions are quite different but MC method is more reliable due to considering more effect of optical matrix.
X axis beam size
at BDC1
X axis beam size
at BDC1

## Slide 23: Beam Study with LiSe++
MC method in IF system (possible up to 2nd order calculation)
Local matrix
(1st order)
Global matrix
(1st order)
2nd order optical matrix is defined here

## Slide 24: Beam Study with LiSe++
MC method in IF system (possible up to 2nd order calculation)
X2
Θ2
Y2
Φ2
L2
δ2
=
X1
Θ1
Y1
Φ1
L1
δ1
1st order
Transformation
Matrix
L : Beam pulse length
δ : Relative momentum dp/p
1st order matrix : 6 x 6
2nd order matrix
In only 1st order matrix,
2nd order elements are empty
2nd order calculation
X2, Θ2, Y2, Φ2, L2, δ2
1st order calculation
X, Θ, Y, Φ, L, δ

## Slide 25: Beam Study with LiSe++
BDC
Plastic Scintillator
Plastic Scintillator
PMT
PMT